## Slide 1
Instructor: Lila Leatherman (they/them)
November 17-18, 2020
Introduction to Change Detection Lecture 2: Image Correction

## Slide 2: Course Agenda
Day 1 – Morning
  10:00-10:45 – Presentation: Course overview and image selection and preparation
  10:30-10:45 – Demonstration: Overview of GEE
  11:00-11:10 – Break
  11:10-11:30 – Presentation: Image correction
  11:30-12:00 – Demonstration: Creating cloud-free composites in EE
Tasks to complete before the next session: Exercise 1 + 2
Day 1 – Afternoon
  2:00-2:30 – Presentation: Band ratios and image transformations
  2:30-3:00 – Demonstration: Identifying significant landscape change
  3:00-4:00 – Q&A and Exercise Help
Tasks to complete before next session: Exercise 3

## Slide 3: Course Agenda
Day 2 – Morning
  10:00-10:45 – Presentation: Image standardizations and image differencing
  10:30-11:00 – Demonstration: Calculating z-scores
  11:00-11:10 – Break
  11:10-11:30 – Presentation: Change thresholding and discussion of accuracy assessment
  11:30-12:00 – Demonstration: Exploring histograms and creating change maps
Tasks to complete before the next session: Exercise 4 + 5
Day 2 – Afternoon
  2:00-2:30 – Q + A and Exercise Help
  2:30-3:00 – Presentation: Change detection applications within USFS
  3:00-4:00 – Final Q + A; help with course-related projects/ideas

## Slide 4: Lecture outline:
Goals of image correction
Components of image correction
  Earth-sun-sensor relationships
  Atmospheric effects
  Surface reflectance
  Cloud-masking
Demo of image correction in GEE

## Slide 5: Image Pre-processing
Goal: Ensure that each pixel records the same type of measurement at the same geographic location through time
  Assumption:
    Spectral properties of non-changed areas are stable
  Motivation:
    Inadequate pre-processing results in false positives

## Slide 6
Variable through time
Influence incident EMR
  Earth-sun distance
  Solar incident angles
  Sensor position
Earth-Sun-sensor relationships
Notes: Three different components, constantly in different positions, and that effects the quality of the reflectance in the image
All images collected come with metadata that include
  Image date
  Time of day
  Other sensor information
All of these affect the reflectance
So we need to calculate
  Distance of earth from sun, based on the day of the year / julian day
    Lots of lookup tables for this
  Solar incident angles and sensor position are included in metadata
You don’t have to do any of this yourself, these corrections and pre-processing are all done on the back end.
  But: still important to understand that they’re happening!

## Slide 7: Reflectance at Top-of-atmosphere
First correction:
Digital Numbers  Radiance  Reflectance (TOA)
Calculated using:
  Sensor calibration coefficients
  Earth-sun distance
  Mean solar exo-atmospheric irradiance
  Solar zenith angle
Top of atmosphere reflectance differs from surface reflectance…
Notes: When we get imagery data, it comes in digital numbers, or DNs
  Eg. Landsat is 8-bit data = 2^8 = 256 different values
  DNs are unitless information – contextual, but don’t apply magnitude
    Eg, colder than yesterday—but doesn’t tell you degrees
  DNs are converted to Radiance, refers to amount of energy. Then convert to reflectance and top-of-atmosphere reflectance – which record the actual magnitude of energy that is being recorded
    TOA – removes all atmospheric effects
    Compared to surface reflectance, which does include atmospheric effects
Behind the scenes, Google Earth Engine uses these parameters to do this pre-processing
    TOA – takes into account the previously mentioned factors and normalizes them to the same scale – reflectance…
    Sensor calibration coefficients: gain, bias
    sensor specific, differences between how hardware records intensity of radiation… ask your local engineer
    Gain = is a multiplier
    Bias = is a shift (plus or minus)
    Mean solar exo-atmospheric irradiance – The irradiance from the sun at the top of the earth’s atmosphere… sun puts out a certain amount of power and…
    There are different ccalculations for that but we use one from Thuillier et al 2003
    All the metadata reports include solar elevation but what you need is solar zenith… which is 90-solar elevation (watch your units- radians vs degrees)

## Slide 8: Atmospheric Effects
  Another source of ‘noise’
  Atmosphere selectively scatters, absorbs and transmits light
Notes:     Scattered, absorbed or transmitted depending on EM wavelength, atmospheric path length and atmospheric conditions
    Atmospheric scatter adds brightness to a scene and to compensate, we will subtract brightness from the scene.
    For change detection, it may be most robust to correct imagery to surface reflectance by compensating for atmospheric effects.

## Slide 9: Surface Reflectance Correction Methods
A few approaches:
  Dark object subtraction (DOS)
  Atmospheric modeling
      Radiative transfer models
  Image-to-image normalization
      Histogram matching
      Regression using pseudo-invariant features
Notes: Two approaches for change detection:
Atmospheric correction: histogram minimum involves calculating stats for eacTry to remove the effects of the atmosphere or simply normalize one image to the other (slave image and reference image)
These are just a
Surface reflectance correction methods
Dark object subtraction
  Straightforward, more common
Atmospheric modeling
  Complex—requires atmospheric data for the time and location where the image was required
Image to image
  Comparing one image to another that were collected in the same area
  Basically, want to use linear regressions to make the images match each other
few examples…

## Slide 10: Dark object subtraction (DOS))
Dark objects can be deep lakes or very dark shadows
  DOS involves identifying the value associated with these areas and subtracting it from all pixels in the image.
Automated using RSAC tools…
Pixel Value
Frequency
Jump
DOS value
Notes:   Theoretically should have zero reflectance
Done for each band
Operates under the premise that dark objects absorb all light, should have a reflectance close to 0
  So if you looked at the reflectance, it should be close to zero across all bands for each pixels
  If the reflectance is higher, you can subtract that increased value from the other reflectance values that you obtain—assuming that those higher values are due to atmospheric effects, so by subtracting them, you subtract out the effects
  Not perfectly accurate because dark bodies get brighter when there are atmospheric effects, and bright things get darker when there are atmospheric effects

## Slide 11: Masking
Clouds and their shadows
  Lead to false positives in change detection.
Snow and water
  Seasonal variation
  Result in false positives (If not part of your research question)
Notes: Remove clouds and their shadows
Do our best to avoid them and we can apply masks to do that work for us
Remove snow and water—not necessarily landcover, just sitting on top of landcover
Fmask cloud algorithm masks the clouds and also their shadows
  We fill in the cloudy areas with images of the same area taken at a different time

## Slide 12: Masking
Cloudy Landsat image
Clouds
Shadows

## Slide 13: Image preprocessing
Function Mask (fmask)
    Identify clouds, shadows and water- Memory intensive process
Exercises 1 + 2 – creating cloud-free composites in GEE

## Slide 14: Image preprocessing
Google Earth Engine can do all of the heavy lifting for us!
Eliminates the manual processing steps
Exercises 1 + 2 – creating cloud-free composites in GEE

## Slide 15: Demonstration
Exercise 2: Cloud-free composites in GEE