## Slide 1: Land Cover Classification Techniques
supervised classification and random forests
Developed by remote sensing specialists at the USFS Geospatial Technology and Applications Center (GTAC), located in Salt Lake City, Utah

## Slide 2: Image Classification
The automated process of categorizing pixels or image objects into a thematic classes (e.g., conifer, deciduous, herbaceous)

## Slide 3: Classification Scheme
Decide on the scheme
  The schema categorizes and labels the land cover theme (e.g. vegetation cover)
  A well-designed classification scheme is critical to deriving acceptable and useful information
  The complexity will affect project accuracy and cost
  It’s not easy—but time spent creating a well designed classification scheme is always well spent!
Notes:   First you choose your “theme”
    Formally defined as a central topic, subject or concept the user is trying to capture.
Note: a theme could be Urban, Transportation, etc. In our case, most of the time our theme will be vegetation cover. And the scheme will be designed around this central theme.
Categorizes and labels the variation in land cover that you wish to capture:
  Based on measurable land cover (not land use) characteristics,
  Based on what the photography can detect
  Avoid interpretive classes such as “Old Growth” or “Suitable Habitat”; these should be derived by definitions based on measurable characteristics,

## Slide 4: IPCC greenhouse gas inventory
Estimate changes in 5 carbon pools for six categories of land use.
The six land use categories include:
Forest land
Cropland
Grassland
Wetland
Settlements
Other land

## Slide 5: The Classification Scheme – 5 rules
Must:
  Be exhaustive:
    All land cover must be accounted for in the legend
    An “Other” category ensures this condition!!
  Be mutually exclusive:
    Each land cover can be assigned to exactly one class
    A land cover feature is considered mutually exclusive if it cannot occur in two classes.
  Be composed of Labels and Rules for labeling
  Meet the user’s needs
  Must be based on what can be interpreted from the imagery (note: this may conflict with the previous requirement in some cases).
Requirements (for continuous cover classifications)

## Slide 6: The Classification Scheme – Suggestions
In addition, the scheme should be:
  Hierarchical
    To be more flexible and better support multiple users.
  Based on measurable land cover characteristics
    Size class, % canopy cover, dominance, etc.
  Avoid subjective, interpretive classes, such as “old growth”.

## Slide 7: Classification Scheme -- Bad Example
Hierarchical?
Exhaustive?
Labeling Rules?
Mutually Exclusive?
No, there is no place for grasslands, mixed forests, etc… an “other” class would satisfy this.
Water
Rock and Soil
Shrub
Forest
  Hardwood
    Sparse
    Medium density
    Dense
  Softwood
    Sparse
    Medium density
    Dense
Regeneration
Yes! The data can be collapsed or expanded.
None! How much tree cover does it take to separate shrub and forest? No definition for density labels.
No! What is “Regeneration”? That could include grasses, shrubs or forest…

## Slide 8: Classification Scheme -- Good Example?
Water
Non-Vegetated (< 20% vegetated)
Rangeland (< 10% tree crown closure)
Forest (> 10% tree crown closure)
  Hardwood (65% of trees are hardwood)
    sparse ( 10% and < 30% CC)
    medium density (30% and < 66% CC)
    dense (66% CC)
  Softwood (65% of trees are softwood)
    sparse (10% and < 30% CC)
    medium density (30% and < 66% CC)
    dense (66% CC)
  Other Forest (includes Mixed)
Other
Notes: This is a better example…
Other ‘Forest’ options-> dense evergreen forests, degraded evergreen forests, dry deciduous forests, mangrove and swamp forest

## Slide 9: Classification Scheme -- Good Example?
Water
Non-Vegetated (< 20% vegetated)
Rangeland (< 10% tree crown closure)
Forest (> 10% tree crown closure)
  Hardwood (65% of trees are hardwood)
    sparse ( 10% and < 30% CC)
    medium density (30% and < 66% CC)
    dense (66% CC)
  Softwood (65% of trees are softwood)
    sparse (10% and < 30% CC)
    medium density (30% and < 66% CC)
    dense (66% CC)
  Other Forest (includes Mixed)
Other
Notes: This is a better example…
Other ‘Forest’ options-> dense evergreen forests, degraded evergreen forests, dry deciduous forests, mangrove and swamp forest

## Slide 10
purple red infrared
This is a graph of a spectral response curves for several different types of material.
It represents the visible to NIR portion of the electromagnetic spectrum
As you can see materials (e.g., dry soil, wet soil) can be identified and differentiated from each other as long as their signatures are unique from one another.
Notes: This is a graph of a spectral response curves for several different types of material.
It represents the visible to NIR portion of the electromagnetic spectrum
As you can see materials can identified and differentiated from each other as long as their signatures are unique from one another.

## Slide 11: Spatial Models
Linking goals (land cover categories)
with
Land cover characteristics (spectral signatures)

## Slide 12: Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate variables
Sample Design
Validation
Fitting/Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 13: Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate variables
Sample Design
Validation
Fitting/Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 14: Components of the Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate Variables
Sample design
Validation
Fitting/Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 15: Predictor Variables
What does water look like?
What does land look like?
What information do you think will help differentiate water from land?

## Slide 16: Predictor Variable Examples
  Impervious surface metric
  Modified normalized difference water index
  Normalized difference vegetation index
  Elevation
  Aspect

## Slide 17: Predictor Variables
Theory/Knowledge to get predictor variables:
Tone/color:
Shape:
Size:
Association:
Shadow:
Pattern:
Texture:

## Slide 18: Spatial Modeling Process
Lidar metrics
Reference Data (ROI)
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate variables
Sample Design
Validation
Fitting/Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 19: Training Data
Required for the advanced classifiers
  Interpreted manually
  Imported from a point or polygon shapefile
    Polygons can end up overlapping multiple segments
    Points are more precise and have less potential for error
Image with samples collected
Classified image

## Slide 20: Required Elements: training data
Sample (training) data considerations:
  Collected in field or digitized from high resolution imagery
  Covers full region
  Full range
  Random, or stratified random is best, often an opportunistic sample is all that is available

## Slide 21: Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate Variables
Sample design
Validation
Fitting/
Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 22: Unsupervised Classification
Conif.
Hardw.
Water
Land Cover Map
Legend
Water
Water
Conifer
Conifer
Hardwood
Hardwood
Labels
After the computer finishes processing, the analyst then attempts to assign these spectral classes into informational classes. It is a simple process to regroup (recode) the clusters into meaningful information classes (the legend).
The result is a Land Cover Map

## Slide 23: Supervised Classification
Digital Image
Supervised classification requires the analyst to create training data, either in the field or from an image data source.
The computer then creates...
Mean Spectral Signatures
Known Deciduous Area
Known Water Area
Known Conifer Area
Water
Conifer
Deciduous

## Slide 24: Supervised Classification
Output Classified Image
Next Pixel to be Classified
Unknown
Mean Spectral Signatures
Conifer
Deciduous
Water
Using the statistical information provided by the training regions, the computer attempts to determine all remaining pixels in the image falling into these defined classes.

## Slide 25: Supervised Classification
Digital Image
Supervised classification requires the analyst to create training data, either in the field or from an image data source.
The computer then creates...
Mean Spectral Signatures
Known Deciduous Area
Known Water Area
Known Conifer Area
Water
Conifer
Deciduous

## Slide 26: Supervised Classifiers
  Nearest neighbor
  Bayes
  Decision Tree
  K-nearest neighbors
  Support Vector Machines
  Random forests

## Slide 27: Classification Process
Classifies based on descriptors applied to the classes
Nearest neighbor
  Select the features the classification will be based on (e.g., red band, NDVI, ancillary data, etc)
  Select training data
Training samples selected for classification

## Slide 28: Decision Trees
Also known as CART (Classification and Regression Tree) when they refer to both:
  Classification tree = predicted outcome is the class to which the data belongs.
  Regression tree = predicted outcome can be considered a real number (e.g. NDVI value)
Data mining technique
Uses training data to develop a tree-like set of rules to determine the class for certain combinations of input data
Simple to use and can produce good results

## Slide 29: Example of a Decision Trees
Landsat Band 4 >120
Landsat NDVI > 350
Aspect > 180
Aspect < 180
Landsat NDVI < 350
shrub
grassland
grassland
For example - separating shrub from grassland

## Slide 30: Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate variables
Sample Design
Validation
Fitting/Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 31
Random Forest
Ensemble-based machine learning technique
  Ensemble = “many of”
  Machine learning technique = Classification and Regression Trees (CART)
  The “Random” in Random Forest describes that the selection of predictor variables is random for any given CART model (“tree”).
= shrub prediction? Yes or No.
Notes: Developed by Adele and Richard Cutler, Dept. of Mathematics, Utah State

## Slide 32
Training or reference data (point data)
  Examples of each class (e.g., Conifer, Aspen, Grass, Shrub, Road, Sagebrush, Shadow, Water, Soils)
Predictor variables such as:
  Multispectral imagery
  Panchromatic imagery
  Topographic variables: Elevation, Slope, & Aspect.
  Bioclimatic variables: Temperature, Precipitation, Moisture Index, Potential Global Radiation, Vapor Pressure, Humidity, Degree Days.
Derived Predictor variables such as:
    NDVI
    Tasseled Cap transformations (soil brightness, greenness, wetness)
What is input into Random Forest?

## Slide 33
CART
Landsat Band 4 >120
Landsat NDVI > 350
Aspect > 180
Aspect < 180
Landsat NDVI < 350
shrub
grassland
grassland
This is an example of 1 Classification tree – hundreds are created randomly using your reference/training data and built for your various Classes.
Random input variables are selected and used on your training data to make trees.
Notes:     Each “tree” is the result of the random selection of input variables (multispectral bands, elevation data, etc.) from the reference data (e.g., image segments or pixels).
  Random Forest makes hundreds to thousands of these Classification trees or decision trees.

## Slide 34
A single CART model created during the Random Forest process.
A single pixel
The CART models make a class prediction for each pixel using the predictor variables that were used as inputs to that particular CART model.
= shrub prediction? Yes or No.
= shrub prediction? Yes or No.

## Slide 35: Spatial Modeling Process
Lidar metrics
Reference Data
Lidar metrics
Predictor Variables: (e.g., image enhancements)
Model
Theory
Map of predicted values
Candidate Variables
Sample design
Validation
Fitting/
Training
Adapted from Guisan and Zimmerman (2000) & Franklin (2009)
Applying Model

## Slide 36
In this example, the most frequently occurring class modeled from the CART models for this pixel is Shrub.
So the final class for that pixel is Shrub.
shrub
shrub
shrub
shrub
shrub
grass
shrub
grass
shrub
grass
shrub
shrub
A single CART model created during the Random Forest process.
A single pixel
Notes: To make predictions:
  Each CART model gets the input data that corresponds to the variables in it’s model to make a predication about which class each segment/pixel should be (e.g., shrub).
  Which ever class gets the most votes, “wins”!
  **Disclaimer: Garbage in = Garbage out

## Slide 37
Input image-cube
(58 layers)
Field & PI training samples
Random Forest models are created & applied
Classification & labeled segments
What comes out of Random Forest?
Inputs
Outputs

## Slide 38: Qualitative assessment of land cover map output

## Slide 39: Ways to improve classification
Improving ROI
Select better predictor variables
Modify land cover class categories
Sieve
Try an object based approach

## Slide 40: Unit of Analysis
Pixel Based Classification
  Uses spectral signatures
  Ancillary data (elevation, etc)
Object Based Classification
  We can use more than spectral information!
  Texture
  Contextual relationships
  Etc.

## Slide 41: Object-based Image Analysis
What is object-based image analysis (OBIA)?
  Image processing technique that uses image “objects” or “segments” as the basic unit instead of pixels

## Slide 42: Object-based Image Analysis
Division of imagery into homogeneous areas
  Image segmentation
Analysis performed on object or segments, not pixels
Especially useful for high-resolution imagery, but beneficial for coarse resolution as well

## Slide 43: Why object-based classification?
Spectral data is averaged for each segment
  Useful when dealing with features that have a range of spectral values (high texture)
Segments filter out “noise” or meaningless information present in individual pixels and groups
  Helps to reveal recognizable features
Increase signal-to-noise ratio
Can improve classification accuracy over pixel-based classification

## Slide 44: Why object-based classification?
Object-based image analysis
  Can use spectral AND other information (size, shape, context, texture, et cetera) for classification
  Eliminates the pixel-based speckling or “salt and pepper” that we sometimes see

## Slide 45: Segmentation
Mean shift
  Most commonly used
  Robust algorithm
  Delineates homogeneous areas
  Memory and processor intensive

## Slide 46: Segmentation
Minimum region size controls the size of the segments
Min region = 50
Min region = 150
Min region = 300

## Slide 47: Segmentation
High variance = small segments
Low variance = large segments

## Slide 48: If you have questions please contact: Karis Tenneson, PhD Remote Sensing Specialist at USFS GTAC krtenneson@fs.fed.us, 801-975-3768 or Brenna Schwert Remote Sensing Specialist at USFS GTAC bmschwert@fs.fed.us, 801-975-3821