## Slide 1: Advanced Change Detection -2 Time Series Analysis

## Slide 2: Housekeeping
Keep video off and stay on mute
If you have questions:
  Raise hand in Teams
  Respond in chat box
  Q + A at the end
Closed captions are available
Take care of your body!

## Slide 3: Course Agenda
Start Time | Content
10:00 am | Lecture 1: Concepts and Image Processing
11:15 am | Break + Exercise 1: Process + Explore Landsat time series
11:20 am | Lecture 2: Adv Change Detection Methods and Products
12:05 pm | Lunch + Exercise 2: Basic trend analysis in EE
1:05 pm | Lecture 3: LandTrendr
1:35 pm | Do Exercise 3 – LandTrendr in EE - Fitting & finding parameters
2:35 pm | Lecture 4: LandTrendr, Change Mapping, and Scripting
2:55 pm | Do Exercise 4 –Run LT-GEE toMap Disturbance
All times MDT

## Slide 4: Lecture objectives
Understand the spectral trajectories associated with different kinds of landscape change
Understand that the analytical method you choose will be determined by the type of change you’re trying to quantify.
Gain exposure to varied change detection methods
Basic understanding of a linear fit change analysis in Earth Engine

## Slide 5: Change analysis with time series
Effective for mapping disturbance patterns
  Look at the big picture
Many different methods
  Two general approaches involved: Look for trends or deviations in the time series
Wikimedia commons
Wikimedia commons

## Slide 6: Temporal dimensions of change
  What does change look like from an Earth observation perspective?
Notes: Remind learners of the temporal dimensions of change, and how lots of factors about the disturbance + our earth observation system will affect how changes can be detected. For example, if we have a satellite with a longer return interval, like Landsat, (particularly if we can’t use cloudy images), we might miss observing particular phenomena

## Slide 7: Temporal dimensions of change
Intra-annual (within-year)
  Seasonal changes (e.g., green-up)
  Drought
  Fire
Inter-annual (multiple years)
  Phenology shift (e.g., earlier green-up)
  Beetle kill
  Urbanization
  Succession + fire recovery
Notes: Some dynamics can only be observed and quantified through multiple observations within a year, or a season. Other dynamics are better understood through multiple observations over multiple years.

## Slide 8: Change & ecology are complex
“Conventional single date (PI) and multi-date approaches have been missing the full picture”
Hermosilla et al 2016
Notes: Key point here to discuss is that methods have been evolving. Use this figure and the points to discuss two date vs. trend vs segmentation.

## Slide 9: Spectral trajectories
Notes: X-axis: time
Y-axis: value of a spectral index, in this case NBR – normalized burn ratio.
These are random trajectories to simulate a couple different scenarios of change (or not).
What does this look like to you? What might cause this trajectory?
The point of this slide is stable trajectory with random noise.

## Slide 10: Spectral trajectories
Notes: X-axis: time
Y-axis: value of a spectral index, in this case NBR – normalized burn ratio.
These are random trajectories to simulate a couple different scenarios of change (or not).
What does this look like to you? What might cause this trajectory?
The point here is stable trajectory with random noise and some noisy noise from a few ‘bad’ images. This is why we mask clouds, etc.

## Slide 11: Spectral trajectories
Notes: X-axis: time
Y-axis: value of a spectral index, in this case NBR – normalized burn ratio.
These are random trajectories to simulate a couple different scenarios of change (or not).
What does this look like to you? What might cause this trajectory?
Point here is slow decline with expected random noise.

## Slide 12: Spectral trajectories
Notes: X-axis: time
Y-axis: value of a spectral index, in this case NBR – normalized burn ratio.
These are random trajectories to simulate a couple different scenarios of change (or not).
What does this look like to you? What might cause this trajectory?
Abrupt change (e.g., harvest, fire, development, etc.)

## Slide 13: Spectral trajectories
Notes: X-axis: time
Y-axis: value of a spectral index, in this case NBR – normalized burn ratio.
These are random trajectories to simulate a couple different scenarios of change (or not).
What does this look like to you? What might cause this trajectory?
Abrupt change with slow, steady recovery.

## Slide 14: What kind of change do we want to capture?
Interannual – long term change
Notes: SOMETHING TO MAKE THE LINK BETWEEN SEASONAL/INTERANNUAL VARIATION TO INTRA-ANNUAL VARIATION? THEN CIRCLING BACK TO MODEL FITTING… ALGORITHMS FUNCTION ON/CAPTURE DIFFERENT TIMESCALES.

## Slide 15: What kind of change do we want to capture?
Interannual – long term change
Intra-annual – includes seasonal dynamics
Notes: ALGORITHMS FUNCTION ON/CAPTURE DIFFERENT TIMESCALES.
If we want to capture intra-annual dynamics, we can fit more complex models that capture the seasonal oscillations, not just an overall trend. Can extract values from these models that help us detect changes in seasonal maxima, minima, averages, etc.

## Slide 16: Spectral trajectories
Remake this slide taken from here: https://prd-wret.s3-us-west-2.amazonaws.com/assets/palladium/production/s3fs-public/atoms/files/LCMAP_workshop_pres3_w_alt_text-3.pdf

## Slide 17: Spectral trajectories
Slide credit: Gorelick et al GEO for Good Summit 2019
Notes: Here is another representation of different forms spectral trajectories can take.
When you begin an analysis, it’s important to know what kind of change you’re attempting to capture– so that you can select a method that’s appropriate to quantify it.

## Slide 18: Separating the signal from the noise
Image selection & processing is the first step
Analysis algorithms seek to do the rest…
  Subtler change signals are harder to separate
  With more data, subtler signals can emerge

## Slide 19: Examples of change:
In the following slides, what kind of change do you see?

## Slide 20
Notes: Camp Fire, northern California. Large burned area, a rapid change with long-lasting effects.

## Slide 21
Notes: Camp Fire, northern California. Large burned area, a rapid change with long-lasting effects.

## Slide 22
Notes: Pando aspen forest. Seasonal changes in foliage color that recur every year. Different years were selected here for image quality / emphasis.

## Slide 23
Notes: Pando aspen forest. Seasonal changes in foliage color that recur every year. This is an example of a seasonal cycle of change. Different years were selected here for image quality / emphasis.

## Slide 24
Notes: Kansas prairie. Two images taken roughly the same time of year, showing drought effects in 2018. This is an example of a single-year deviation that represents a change to the normal seasonal cycle, and should be more or less back to “normal” the following year (barring cascading effects)

## Slide 25
Notes: Kansas prairie. Two images taken roughly the same time of year, showing drought effects in 2018. This is an example of a single-year deviation that represents a change to the normal seasonal cycle, and should be more or less back to “normal” the following year (barring cascading effects)

## Slide 26: Examples of change:
- All of these changes are represented here as the difference between two dates– but would look very different when represented as time series!

## Slide 27: Time series methods
There are many new algorithms for analyzing Landsat time series:
  “…sophisticated workflows that consist of a logical sequence of processes and rules, multiple statistical functions, and parameter sets that must be calibrated to accurately classify disturbance.”
    -Cohen et al 2018
Advantages and disadvantages to different methods

## Slide 28: Time series methods
Algorithm | Time Series | Targeted Disturbance | Basic Approach | Environment
LandTrendr | Annual | Forests only. Events and trends. | Temporal segmentation | EE
CCDC | All images | All cover types. Events. | Multi-year departures | EE
EEWMACD | All images | Forests only. Events. | Multi-year departures | EE
VCT | Annual | Forests only. Events. | Multi-year departures | EE
VeRDET | Annual | Forests only. Events and trends. | Spatial and temporal segmentation. | EE
ITRA | Annual | Woody vegetation. Gradual trends. | Slope through time | Not in EE
MIICA | Annual | All cover types. Events. | Bi-temporal differencing | Not in EE
Table adapted from: Cohen et al 2017
Notes: All of these are pixel-based time series methods:
LandTrendr (Landsat-based detection of trends in disturbance and recovery)
ITRA (Image trends from regression analysis)
VCT (Vegetation change tracker)
EWMACD (Exponentially weighted moving average change detection)
MIICA (Multi-index integrated change analysis)
CCDC (Continuous change detection and classification)
VeRDET (Vegetation regeneration and disturbance estimates through time)
Though several of these algorithms are implemented in Earth Engine, LandTrendr is the best documented and most stable with CCDC quickly becoming more established.

## Slide 29: CCDC
Continuous Change Detection and Classification
    Pixel-based analysis of ALL Landsat data
    Fits models using sines and cosines
    Identifies breaks (change)
    Classifies landcover
  Inputs
    All available clear Landsat observations
Learn more about the algorithm from LCMAP or Zhu et al 2014

## Slide 30: CCDC
LCMP CCD Algorithm Description Document 2020

## Slide 31: CCDC
LCMP CCD Algorithm Description Document 2020

## Slide 32: Simple time series change detection in EE
Calculate linear regression
  “computes the least squares estimate of one variable with a constant term”
Inputs:
  Time series of images
  Images have two bands: variable of interest, and time
    E.g., change in NBR over time
Outputs:
  Image with 2 bands representing slope and intercept

## Slide 33: Simple time series change detection in EE
spectral index
time
spectral index
time
Adapted from the LT-GEE Guide
Notes: We are fitting a linear regression to a time series of images, in order to assess a simple version of change over time.
Specifically, we’re fitting a separate regression model to each pixel in the time series.
The quantitative outputs of this model are, for each pixel, the slope and the intercept.

## Slide 34: Simple time series change detection in EE
- slope
- intercept
spectral index
time
spectral index
time
Adapted from the LT-GEE Guide
Notes: We are fitting a linear regression to a time series of images, in order to assess a simple version of change in one variable over time.
Specifically, we’re fitting a separate regression model to each pixel in the time series.
The quantitative outputs of this model are, for each pixel, the slope and the intercept.

## Slide 35: Simple time series change detection in EE
Example: linearFit() method applied to projected precipitation, 2000-2050.
  blue = more precip , red = less precip
Value of the slope is used for visualization parameters
via GEE documentation for Linear Regression

## Slide 36: Simple time series change detection in EE
Trends in city lights in Mexico City 1992-2014
green = increase, red = no change, blue = decrease
Adapted from code by Jamon Van Den Hoek
Notes: Let’s also add the code to this example.

## Slide 37: Landsat-based detection of trends in disturbance and recovery (LandTrendr)
Pixel-based temporal segmentation of annual time series
Inputs
  Annual time series (doesn’t look at change within a year)
  Set of parameters
Outputs
  Annual info about change segments, fitted values
  Can be used to identify timing, duration, and speed of landscape change
  Can be processed into pixel-based time series, maps of disturbance
Link to original paper: Kennedy et al 2010
Notes: Option to introduce LandTrendr here… but might distract from description of simple time series analysis.

## Slide 38: Exercises for today
Exercise 1: Process and explore Landsat time series
  Optional – review image processing in GEE
Exercise 2: Basic trend analysis
Exercise 3: LandTrendr in GEE: Model fitting
Exercise 4: LandTrendr in GEE: Disturbance mapping
Notes: I have repeated this slide in each to remind students of where we are and where we are going.

## Slide 39: Demo + Exercise 2
Basic trend analysis
Open script from exercise 1
Transform a time series to create vegetation indices
Plot a time series as a chart
Use a native EE function to perform a linear trend analysis

## Slide 40: Demo
In another, non Dixie NF area:
  Pixel
    Start with known point and run with default parameters
    Adjust seasonal windows to get good start/stop
    Show despiking