## Slide 1: Using Lidar Data in ArcGIS Pro
Indigo Catton
Remote Sensing Analyst
indigo.catton@usda.gov
(801) 975-3452

## Slide 2: Housekeeping
USDA Forest Service- Geospatial Technology and Applications Center (GTAC)
  Instructor: Indigo Catton, contractor
  Introductory course
    Experience with Pro will be helpful
    A basic understanding of Lidar is helpful but not necessary
Salt Lake City

## Slide 3
Take a break!

## Slide 4: Schedule
Presentation and Demonstration: 10:00 am - 11:00 am
Exercises 1&2: 11:00 am - 12:00 pm
Presentation and Demonstration: 12:00 pm - 1:00 pm
Exercises 3, 4 & 5: 1:00 pm - 4:00 pm

## Slide 5: Please Interact!
If dialed into teleconference:
  Please mute your phone
  Do not put the call on hold
Question or comments?
    Unmute by dialing *6
    Send a chat
    Send a personal chat
    Brenna Schwert will help answer questions on chat.

## Slide 6
The goals of this training
  Brief introduction to lidar
  Learn the capabilities of lidar data in Pro
  Learn basic LAS Dataset processing functions in ArcGIS Pro
If you’re unfamiliar with lidar, you should explore GTAC’s lidar courses:
  https://usfs.adobeconnect.com/p93bl180pa76/
Before We Start
Notes: What is lidar?
Using lidar
File Formats
Lidar in ArcGIS Pro Pros and Cons

## Slide 7: What is lidar?
Light Detection and Ranging (LiDAR)
  Uses laser pulse to measure distance from lidar sensor to an object
  Scanning angle and distance to create georeferenced data points
Collects hundreds of thousands or millions of points per second.

## Slide 8: What is lidar?

## Slide 9: What is lidar?

## Slide 10: Lidar Data Characteristics
Raw Lidar Data Resolution
  We use pulse density (pulses/m2).
  Quality Level, QL1
  ≥ 8 pulses/m2
1 pulse/meter
8 pulses/meter

## Slide 11: Lidar Data Characteristics
Pulse Density and Point Density

## Slide 12: Lidar Data Characteristics
All returns (100%)

## Slide 13: Lidar Data Characteristics
All returns (100%)
1st returns (69%)

## Slide 14: Lidar Data Characteristics
All returns (100%)
1st returns (69%)
2nd returns (26%)

## Slide 15: Lidar Data Characteristics
All returns (100%)
1st returns (69%)
2nd returns (26%)
3rd returns (4%)

## Slide 16: Lidar Data Characteristics
All returns (100%)
1st returns (69%)
2nd returns (26%)
3rd returns (4%)
4th returns (<0.1%)

## Slide 17: American Society for Photogrammetry and Remote Sensing (ASPRS) Classification codes LAS format 1.1-1.4 https://www.asprs.org/wp-content/uploads/2010/12/LAS_1-4_R6.pdf
Classification Value | Meaning
0 | Never Classified
1 | Unclassified
2 | Ground
3 | Low Vegetation
4 | Medium Vegetation
5 | High Vegetation
6 | Building
7 | Low Point
8 | Reserved
9 | Water
10 | Rail
11 | Road Surface
12 | Bridge Deck
13 | Wire- Guard
14 | Wire- Conductor
15 | Transmission Tower
16 | Wire-structure Connector
17 | Reserved
18-63 | Reserved
64-255 | User definable

## Slide 18: Using Lidar
Many forestry lidar projects will follow a similar workflow:
  Project planning – choosing study area
  Flying lidar (vendors typically preprocess data)
  Explore your data
  Run a quality check on your data
  Create first order metrics
  Create second order metrics, if necessary
  Final analysis

## Slide 19: Using Lidar
Many forestry lidar projects will follow a similar workflow:
  Project planning – choosing study area
  Flying lidar (vendors typically preprocess data)
  Explore your data
  Run a quality check on your data
  Create first order metrics
  Create second order metrics, if necessary
  Final analysis

## Slide 20: Using Lidar
Many forestry lidar projects will follow a similar workflow:
  Project planning – choosing study area
  Flying lidar (vendors typically preprocess data)
  Explore your data
  Run a quality check on your data
  Create first order metrics
This course focuses on how to use ArcGIS Pro to accomplish these tasks

## Slide 21: What is .las?
LASer file format (.las)
Specified by American Society for Photogrammetry and Remote Sensing (ASPRS)
Public binary file for storing point cloud data
Current version is 1.4

## Slide 22: What is a LAS Dataset?
A LAS Dataset (.lasd) is NOT a .las file
For the most part .lasd files cannot manipulate the raw lidar data
A LAS Dataset is a reference to the .las files, and allows points to be displayed in ArcGIS

## Slide 23: What is a LAS Dataset?

## Slide 24: Using lidar with ArcGIS Pro
ArcGIS Pro needs to have a LAS Dataset to use lidar data
  With the exception of several tools, some of which you’ll use in the exercises.
ArcGIS Pro allows some lidar products to be created from a LAS Dataset
  DEM, CHM, height metrics, and canopy density
Dedicated lidar software still has greater functionality

## Slide 25: Using lidar with ArcGIS Pro
Advantages of working with lidar data in ArcGIS Pro
  Simple, built in functions for filtering points
  Tools are available for assessing the quality of the lidar data
  Tools are available for creating some rasters (first order metrics) from filtered LAS Dataset

## Slide 26: Using lidar with ArcGIS Pro
Disadvantages of working with lidar data in ArcGIS Pro
  Cannot manipulate the raw .las file
  Some advanced metrics cannot be easily created
    Lidar is useful for measuring vegetation height and density. ArcGIS Pro’s tools more easily focus on height
Biomass
R²=.88
Total Basal Area
R²=.78

## Slide 27: ArcGIS Pro Capabilities
Use | ArcGIS Pro | Other
Lidar Visualization |  | 
GIS ready rasters (DEM) |  | 
Editing .las files | (Some) | 
First Order Metrics | (some) | 
Modeled Second Order Metrics (biomass, basal area etc.) |  | 

## Slide 28: Today’s Exercises
Morning
  Exploring and visualizing lidar data
  Data Quality checks
Afternoon
  Creating basic hydrology products
  Creating vegetation metrics
  Create canopy density products

## Slide 29: Schedule
Presentation and Demonstration: 10:00 am - 11:00 am
Exercises 1&2: 11:00 am - 12:00 pm
Presentation and Demonstration: 12:00 pm - 1:00 pm
Exercises 3, 4 & 5: 1:00 am - 4:00 pm

## Slide 30: Questions?