## Slide 1: Introduction to Change Detection Tools
Instructor: Brenna Schwert
November 6-7, 2019

## Slide 2: Introduction
Image Differencing
  Two-date method of locating change
Input types:
  Bands
  Classification
  Transformations

## Slide 3: Spectral Image Enhancements
Simple mathematical:
Complex spectral:
Ratio =
Band1
- Band 2
Band1
+ Band 2

## Slide 4: Review of Spectral Signatures
Graphically, the spectral reflectance of green vegetation in the visible wavelengths may be represented as shown...
Notes: We can take advantage of band ratios in 2 ways:
1st, discrimination of vegetation vs. non-vegetation areas, or classifying vegetation, water, urban areas, bare soil, etc.

## Slide 5: Review of Spectral Signatures
Graphically, the spectral reflectance of green vegetation in the visible wavelengths may be represented as shown...
Notes: We can take advantage of band ratios in 2 ways:
1st, discrimination of vegetation vs. non-vegetation areas, or classifying vegetation, water, urban areas, bare soil, etc.

## Slide 6: Review of Spectral Signatures
Graphically, the spectral reflectance of green vegetation in the visible wavelengths may be represented as shown...
Notes: We can take advantage of band ratios in 2 ways:
1st, discrimination of vegetation vs. non-vegetation areas, or classifying vegetation, water, urban areas, bare soil, etc.

## Slide 7: Review of Spectral Signatures
As vegetation becomes unhealthy, the reflection of the EMR changes.
Notes: 2nd: As vegetation becomes unhealthy or senesces, its response to near-IR wavelengths is reduced, similar to how we see here.

## Slide 8: Review of Spectral Signatures
As vegetation becomes unhealthy, the reflection of the EMR changes.
Notes: 2nd: As vegetation becomes unhealthy or senesces, its response to near-IR wavelengths is reduced, similar to how we see here.

## Slide 9: Band Ratios
Sensors capture discrete spectral information in ‘bands’ in a small portion of the full spectrum.

## Slide 10: Band Ratios
We can read these values for each pixel, and then do the math for each pixel throughout the entire image.

## Slide 11: Band Ratios
The simple vegetation ratio is simply Red / NIR, and would be:
43/183 = 0.23

## Slide 12: Normalized Difference Vegetation Index
We make use of the spectral response of vegetation to obtain information about the vegetation…
Notes: For NDVI, we look again at the red and NIR bands.

## Slide 13: Normalized Difference Vegetation Index
Response to EM Energy
We make use of the spectral response of vegetation to obtain information about the vegetation…

## Slide 14: Normalized Difference Vegetation Index
Response to EM Energy
NDVI is lower for unhealthy vegetation
Notes: [Watch the multiple animations in this slide. Let them work, and then describe; don’t anticipate.]

## Slide 15: Normalized Burn Ratio (NBR)
Works on a similar concept as NDVI
The red band is replaced with a short-wave infrared (SWIR) band
  Band 7 for Landsat
  Most other sensors have a corresponding band
Improved method for delineating burned areas

## Slide 16: Normalized Burned Ratio (NBR)
Burned vegetation has a much different response curve.

## Slide 17: Normalized Burned Ratio (NBR)
We typically use the differenced NBR (dNBR) to provide a quantitative measure of absolute change

## Slide 18: Band Ratios
We take advantage of these ratios to extract information from the imagery
Several indices have been created for vegetation analysis based on band ratios.
The following are a brief survey of indices based on Landsat bands:
Index name | Equation | Use
NDVI | (B4 – B3) / (B4 + B3) | Vegetation health
Moisture Stress Index | B5 / B4 | Indicates stress due to low moisture amounts
Leaf Water Content | -log(1- (B4-B5)) / -log(1-(B4’-B5’)) | Assess water stress
Soil Adjusted Vegetation Index | ((1+L)*(B4–B5)) / (B4+B5+L) | Removes effect of soil within pixel; value of L can vary, but 0.5 is typical
Atmospherically Resistant Veg. Index | B4-(B3-(B1-B3)) / B4+(B3-(B1-B3)) | All terms use a special atmospherically corrected value.
B4’ and B5’ indicate response when leaves are at max water content

## Slide 19: Image Transformations
What are they?
  Linear transformation of multidimensional data
    Applies scalars and constants
    e.g., principal components
  Reduces data dimensionality
  Captures as much variation in the data as possible in two or three bands
  Typically done with data with much higher dimensionality.
Notes: Move this to talk 4!
Like principal components but components are related to geophysical properties of the scene. First component is ‘soil brightness’, second component is ‘greenness’ and the third component ‘wetness’.
  Explain feature space – pixel
This transformation reduces the Landsat reflectance bands to three orthogonal indices called brightness, greenness and wetness

## Slide 20: Image transformation – Tasseled Cap
  Extracts components related to geophysical properties
  First 3 bands of new image
    Brightness
    Greenness
    Wetness (third orthogonal axis)
  Uses coefficients specific to sensor
Linear spectral transformation
Notes: Move this to talk 4!
Like principal components but components are related to geophysical properties of the scene. First component is ‘soil brightness’, second component is ‘greenness’ and the third component ‘wetness’.
  Explain feature space – pixel
This transformation reduces the Landsat reflectance bands to three orthogonal indices called brightness, greenness and wetness

## Slide 21: Image transformation – Tasseled Cap
7-band Landsat TM5 image
3-band Tasseled Cap image
Brightness
Greenness
Wetness
Notes: Upper right image: we normally use red, green, blue, or NIR, red, green as shown here to view data.

## Slide 22: Using image enhancements to map change
In Exercise 3, you will
learn how to create band ratios and image transformations using ArcGIS
investigate how certain landscape features appear through the lenses of different image enhancements
observe differences in images/bands when landscape changes have occurred

## Slide 23: Demonstration
Image Enhancements in ArcGIS