## Slide 1: Introduction to Change Detection Tools
Instructor: Brenna Schwert
November 6-7, 2019

## Slide 2: Software and Data for Exercises 4 & 5
Required Software:
    ArcGIS 10.x
Required Data for Exercises 4:
    Outputs from exercise 3
Required Data for Exercise 5:
    Outputs from exercise 4

## Slide 3: Creating a change map
Review:
  You have learned how to select and prepare your data and analyze spectral changes…
Next steps:
  Create difference image
  Standardize difference image
  Threshold standardized difference image
  Evaluate change output

## Slide 4: Image Differencing
Use raster math to calculate a difference image
    Pixel values in change image represent spectral change (positive/negative)
-
=
Time 1 - Time 2
Difference Image
Time 1
Band n, Image A
Time 2
Band n, Image B
Notes: In the difference image, positive and negative values represent increases or decreases in brightness…

## Slide 5: Means of conducting change detection
Kennedy et al. 2009
Notes: Kim – get figure for “drilling through” a pixel through a time series

## Slide 6: Image Standardization
How do we standardize our data?
    Radiometric and atmospheric corrections
    Image enhancements, such as NBR and NDVI
    Calculating Z-scores
Why is this important?
    Accounts for differences between images
      Illumination, time, space
    Allows for the direct comparison of images
    Creates direct measurements that are transferable across studies

## Slide 7: The Standard Score (z-score)
can be calculated from the raw difference values using the equation below, where x represents the difference value for each pixel, and the Greek letters mu and sigma represent the estimated (observed) mean and standard deviation of the difference in land pixels.

## Slide 8: Demonstration
Image Differencing and Calculating z-scores

## Slide 9: Objectives
Gain awareness of image differencing techniques
Understand the need to standardize data
Explore histograms of difference images
Gain awareness about different thresholding options
Review accuracy assessment options

## Slide 10: Image Differencing

## Slide 11: Change Histograms
Distribution of pixel values in change image (Time1-Time2)
    Rarely will a pixel have exactly the same value in both images
    Changed pixels deviate most from the central tendency
Classify change in pixels to separate “real change” from noise.
    E.g., apply thresholds
0 (no change)
Notes: Even if images are well corrected and well matched, rarely would we expect a pixel to have the same value in time 1 and time 2 images. The distribution of change pixel values will most likely follow normal distribution, with the mean pixel value centered on zero and ‘true change’ depicted by pixels some distance from this mean.

## Slide 12: Change Thresholding
Manual
    Hand digitizing
    Manual threshold placement
Automated
    Algorithm placement
    Defined thresholds based on empirical research
Semi-automated
    Classifying change

## Slide 13: Evaluation of Change Maps
In spite of our efforts, change maps likely contain errors…
Accuracy assessment – Evaluate the correctness of the change map produced
  Compare the change map to reference data
    Independent training and reference data
  Many assessment options depending on goals and resources
Notes: Careful analysis and post-processing can improve accuracy.
Change maps will still likely contain errors and these should be addressed in an accuracy assessment.
Does my map agree with reference data… It’s not really an accuracy assessment, it’s an agreement assessment… Reference data can have problems

## Slide 14: Importance of Accuracy Assessments
Accuracy assessments are essential parts of all modeling exercises, remote sensing or otherwise.
They allow users to compare different change detection approaches.
They provide information on the reliability and usefulness of change detection techniques
They support the use of change map for decision-making.

## Slide 15: Site vs. Non-Site Specific Accuracy
Non-Site
  No locational component
  Total acreage by category comparison between a change map and some reference data (e.g. FIA data)
Site
  Locational/Spatial component
  Use of error matrix to represent errors of omission and commission of change (spatial error)

## Slide 16: Non-Site Specific Accuracy
Reference Data
Classified Image #1
Classified Image #2
Change = 1,000 acres
Change = 1,200 acres
Change = 1,200 acres

## Slide 17: Change Map- Error Matrix
CH = Changed
NCH = Not Changed
Notes:   Quantify errors in an error matrix
    Error matrix:
      Overall accuracy, co-mission and omission

## Slide 18: Change Map- Error Matrix
CH = Changed
NCH = Not Changed
Overall Accuracy =
27 + 63 = 90
90/100 * 100 = 90%
Notes:   Quantify errors in an error matrix
    Error matrix:
      Overall accuracy, co-mission and omission

## Slide 19: Change Map- Error Matrix
Notes:   Quantify errors in an error matrix
    Error matrix:
      Overall accuracy, co-mission and omission

## Slide 20: Site Specific Accuracy - Summary
It’s more complicated than simply reporting overall accuracy…
  Consider the relative costs of omission vs commission errors
  These considerations should influence your choice of analysis methods, thresholds, post processing steps, etc.

## Slide 21: Limitations
Doesn’t consider the accuracy of the change blob boundaries
With multiple change classes:
  Makes no distinction for the magnitude of error
  Assumes each site can only be assigned to one map category
Notes: It’s a little wrong to call a tomato a vegetable, it’s a lot wrong to call a tomato a hammer… (James cannot take complete credit for this quote, as much as he would like to.)

## Slide 22: Assessment Options
Best Option –
  Quantitative evaluation with field-collected reference data – many points from a designed sample (i.e., stratified vs. random).
    Requires time, money and resources.
Mid-level Option –
  Computer validation of the map, using ancillary GIS layers and photo interpretation.
  Qualitative assessment of map product in the field.
Low-level option
  No quantitative/qualitative accuracy assessment is done of the map product… Rather, quality of the product is inferred by the quality of the process.
    Assumption: If the logic and data are sound, the output are reasonable

## Slide 23: Demonstration
Exploring Histograms and Creating Change Maps