## Slide 1: Introduction to Change Detection Tools
Instructor: Brenna Schwert
November 6-7, 2019

## Slide 2: Housekeeping
Instructor: Brenna Schwert
    Remote Sensing Specialist & Senior Trainer
    On-site contractor
    USDA Forest Service, Geospatial Technology and Applications Center (GTAC)
Suggested Experience:
    Basic working knowledge of ESRI’s ArcMap
    Some foundation in remote sensing

## Slide 3: Adobe Connect & Teleconference Basics
Adobe Connect
  Quick orientation to interface
  Different layouts
Please dial *6 to mute your phone
  Question or comment?
    Un-mute by dialing *6 again
    “Raise” your hand
    Send a chat

## Slide 4: Software and course data
Required Software:
    ArcGIS 10.x
Suggested Software
    Google Earth Engine account
Course data
    Available via the tutorial or agenda (unnecessary with GEE account)
      Cloud_Free_Composites.zip
    Contents:
      Landsat imagery

## Slide 5: Outline and Course Agenda
Day 1:
  Concepts and overview
  Scene selection and image pre-processing
  Identifying change: Spectral characteristics of change
Day 2:
  Measuring and mapping spectral change
  Classifying and validating change
More details in the course agenda!

## Slide 6: Introduction to Change Detection
Course objectives
  Establish a conceptual foundation
  Increase awareness of applications and capabilities
  Acquire a conceptual and technical toolset enabling you to conduct/evaluate change analyses

## Slide 7: What is Change Detection?
Identifying landscape change from remotely sensed images
    Analyze images from different times to map/quantify change
    Assumption:
      Landscape change -> Spectral change
Coconino NF – Schultz fire effects
Landsat TM5 image – 1 year post fire

## Slide 8: What is Change Detection?

## Slide 9: What is Change Detection?

## Slide 10: What is Change Detection?

## Slide 11: What is Change Detection?

## Slide 12: What is Change Detection?

## Slide 13: Monitoring Change with Remote Sensing
Satellite and aerial sensors provide:
  Consistent, repeatable measurements
  An ever-growing archive of imagery
  Several sensors/image programs available with different spatial scales, spectral resolutions and return intervals
SPOT
MODIS
Landsat

## Slide 14: Review - Optical Remote Sensing Basics
Conifer
Asphalt
Water
Remote sensing relies on the fact that different targets have unique responses to Electromagnetic (EM) energy
We can distinguish land-cover types spectrally and track them through time

## Slide 15: How do we detect change from imagery?
Changes on the landscape can be detected as changes in the ‘spectral space’ occupied by an image pixel
0.4
Wavelength (µm)
2.6
Reflectance
Healthy Vegetation
Burned Vegetation

## Slide 16: Change Agents
Natural or anthropogenic
    Change agents affecting forests:
      Wildfire, insect outbreaks, succession, drought or climate change, regeneration, storms, etc.
      Harvest, management, agriculture, development, invasive species, etc.

## Slide 17: Dimensions of Change
Changes occur across variable spectral, spatial and temporal scales
Temporal
Spatial

## Slide 18: Sensor Characteristics
Sensor Name | Number of Bands | Spatial Resolution | Temporal Resolution | Radiometric Resolution | Area/Scene (km2)
MODIS | 36 | 250m, 500m, 1000 m | *1 day | 4096 | 2330 “swath”
Landsat 4-5 MSS | 4 | 80 m | 16 days | 256 | 31,450
Landsat 5 TM | 7 | 30 m | 16 days | 256 | 31,450
Landsat 7 ETM+ | 8 | 30 m | 16 days | 256 | 31,450
SPOT 5/Pan | 3/1 | 20 m/10 m | *2-3 days/2-3 days | 256/256 | 3600/3600
IKONOS/Pan | 4/1 | 4 m/1 m | ~3 days/~3 days | 2048/2048 | 190/128
QUICKBIRD/Pan | 4/1 | 2.4 m/0.6 m | 2-11 days/2-11 days | 2048/2048 | 272/272

## Slide 19: Analysis Prerequisites
Clearly define objectives
  Identify the problem:
    Change phenomena of interest (e.g., fire effects, forest mortality, stream channel changes, etc.)
    Define study area
    Determine frequency for change analysis (e.g., seasonal, annual, biennial, etc.)
    Consider limitations
These considerations determine appropriate methods and whether or not change can even be detected

## Slide 20: Approaches
Manual
    Image interpretation
Automated
    Two-date change detection
      pre and post imagery
    Trend analysis
      Multi-temporal image stacks
Prefire
Postfire
Change
Time

## Slide 21: Two-date Change Detection
Prefire
Postfire
Change
Multiple approaches with common core concepts:
  Identify spectral characteristics of significant change and separate it from noise
Focus of this course:
  Two-date image differencing
  Moderate resolution satellite imagery
  Provides a foundation for other methods
  Can be accomplished using readily available tools
Notes:   Examples of different approaches: Post classification, z-score analysis, simple image differencing, etc.
  Different approaches are appropriate for different situations; however, all share some common core concepts.
“Kennedy et al 09, Despite the variety of methods, most change detection approaches contain a modeling phase or a functional algorithm and a subtraction phase”

## Slide 22: Challenge
Separate real change from spectral change caused by:
  Seasonal variation and phenology
  Image misregistration
  Clouds and shadows
  Radiometric inconsistencies
      Sensor
      Variability in illumination (sun-angle, sensor position)
      Atmospheric effects
Notes: Detecting landcover change by mapping spectral change presents the challenge of separating ‘significant’ change from ‘noise’

## Slide 23: Two-Date Methods Overview
Data selection and acquisition
    Imagery and reference data
Image processing and enhancement
    Correction, normalization and transformation
Analysis
    Quantify differences and create a change map
Evaluation
    Accuracy assessment

## Slide 24
Select imagery
Correct and normalize Images
Co-register images
Transform images
Compute Difference Image
Threshold change and Filter results
Evaluate results
Time 1 - Image
Final Change Image
Difference Image
Transformation Time 1
Transformation Time 2
Time 2 - Image
Notes: Copy to work on

## Slide 25: Image Selection - Overview
Four primary considerations
  Type, timing, quality, cost
Goals:
  Capture the change of interest
    Consider image and change phenomenon resolution (spatial, temporal and spectral)
  Minimize non-target change or ‘noise’
    Select near anniversary dates to minimize illumination and seasonal differences
Notes: Minimize extraneous factors to isolate changes of interest

## Slide 26: Imagery - Spatial Considerations
Spatial resolution (pixel size)
Extent
Trade-off between resolution and extent
Simulated MODIS, Landsat, SPOT and
WorldView-2 data.
WorldView-2 2m
SPOT 5 10m
Landsat 7 30m
MODIS 250m
Notes: Consider the type of change that you want to map… Can’t see single trees in a Landsat pixel, can’t even really see ‘stands’ in a MODIS pixel… explain pixel mixing
Spatial grain is the area on the ground captured by a single sensor element, effectively the pixel size.
Extent is the geograhic scope of an image, the satellite footprint
Spatial grain of a sensor is the area on the ground captured within a single sensor element, effectively the pixel size.
The extent is the geographic scope of an image

## Slide 27: Imagery - Temporal Considerations
Seasonal and environmental effects (e.g., soil moisture, phenology)
Persistence of change phenomena
  (i.e., consider recovery and succession)
Figure adapted from Kennedy et al 2007
Seasonal mismatch - World View2
September 2011
March 2011
Notes: Image timing must be chosen to minimize the influence of unwanted effects on spectral space,since such effects obscure real change or produce the false appearance of change. Key issues to consider are phenological state of the landscape, sun angle
Temporal grain is the frequency at which images of a given point on the earth are acquired (Kennedy et al 2009)

## Slide 28: Image Preprocessing
  Geometric
    Co-registration
      Pixel-to-pixel alignment is especially important for image differencing
  Image Correction
    Correct or normalize the spectral values in the image pair
Notes:     Careful preprocessing of image pairs is required
    Minimize spurious changes facilitating the identification of ‘true’ change

## Slide 29: Effects of Registration Errors
Co-registered
Not co-registered
Notes: Notes: One study (Dai and Khorram 1998), found that to achieve 10% or less errors, co-registration of 0.2 pixels or better was required. DeltaCue requires (or recommends) better than ½ pixel co-registration.
Accurate and consistent georeferencing is especially important for automatic land cover change algorithms because change detection is performed by overlaying images from different dates. If shifted even slightly, the overlay will show many false changes that are artifacts of the georeferencing error and not due to actual changes in the landscape.

## Slide 30: Image Correction
Radiometric
    Sensor calibration, illumination and view angle
Atmospheric
    Selective scattering and absorption of light alters reflectance
Notes:     It’s really important to convert digital numbers (DNs) or brightness values recorded by the sensor to meaningful physical units such as reflectance. Depending on the project objectives, it may be desirable to also try to correct for atmospheric effects but this is more difficult and not always done.
Talk about DNs:
DN- Brightness value-initial value that gets recorded by the sensor (analagous to zeros and ones, it’s a record, it’s a marker… makes ); however, in order to
      Haze
      Sun angle
      Water vapor
Talk about atmospheric gases and aerosols –

## Slide 31: Image Enhancement or Transformation
Derive and compare attributes highlighting scene features of interest
  E.g., NDVI, NDMI, Tasseled Cap Greenness layers
Advantages:
  Reduce data and noise
  Simplify comparisons
Notes: You should select those that help to hone in on your change phenomenon of interest

## Slide 32: Normalized Difference Vegetation Index (NDVI)
4band image NAIP image
Single band NDVI image
NDVI = (NIR – Red) / (NIR + Red)
Vegetation appears bright (high values)
Non-vegetation appears dark (low values)
1m NAIP imagery – 4band (blue, green, red, NIR)
1m NAIP NDVI – 1band (NDVI)
Notes: Take this slide and adapt for band ratio talk? Add the actual NDVI values for non-veg, veg, etc.

## Slide 33: Change Analysis- Image Differencing
Use raster math to calculate a difference image
    Pixel values in change image represent spectral change (positive/negative)
-
=
Time 1 - Time 2
Difference Image
Time 1
Band n, Image A
Time 2
Band n, Image B
Notes: In the difference image, positive and negative values represent increases or decreases in brightness…

## Slide 34: Change Analysis - Image Differencing
Example:
  Normalized Burn Ratio (NBR) = NBR = (NIR – SWIR) / (NIR + SWIR)
  Difference NBR = dNBR = Pre NBR – Post NBR
  Burn Severity = Thresholds applied to dNBR
Pre-fire
Post-fire
Landsat
NBR
dNBR
Difference
Threshold applied -
Burn Severity
6/8/2005
6/14/2007

## Slide 35: Analysis – Thresholding
Partition change image (change/no change)
Example – Landsat NDVI difference image and a threshold of 2 standard deviations (+/-)
Vegetation Decrease
Vegetation Increase
Notes: NDVI image difference of forest north of the uintas. Forest harvests show up clearly as decreases in NDVI

## Slide 36: Validation– Accuracy Assessment
Evaluate change maps using reference data
Landsat Derived Change Map
High Resolution Reference Imagery (Pre and Post)
Notes: Put the TARDIS in here
  Multiple assessment options depending on project goals and resources
      Quantitative
      Qualitative

## Slide 37: Change Detection - Summary
Many considerations and approaches
    Manual, automated, two-date and trend analysis methods
A multistep process
    Image selection/acquisition, preprocessing, enhancement/transformation, mapping change, validation
Notes: Additional relevant training
    Available through RSAC, ask us for recommendations!

## Slide 38: Overall Goal: In a Nutshell
Minimize noise and map spectral change that represents significant landscape change

## Slide 39: Demonstration
Overview of GEE