## Slide 1: Introduction to Change Detection Tools
Instructor: Brenna Schwert
November 6-7, 2019

## Slide 2: Image Pre-processing
Goal: Ensure that each pixel records the same type of measurement at the same geographic location through time
  Assumption:
    Spectral properties of non-changed areas are stable
  Motivation:
    Inadequate pre-processing results in false positives

## Slide 3: Earth-Sun-sensor relationships
Variable through time
Influence incident EMR
  Earth-sun distance
  Solar incident angles
  Sensor position

## Slide 4: Reflectance at Top-of-atmosphere
First correction:
Digital Numbers  Radiance  Reflectance (TOA)
Calculated using:
  Sensor calibration coefficients
  Earth-sun distance
  Mean solar exo-atmospheric irradiance
  Solar zenith angle
Top of atmosphere reflectance differs from surface reflectance…
Notes:     TOA – takes into account the previously mentioned factors and normalizes them to the same scale – reflectance…
    Sensor calibration coefficients: gain, bias
    sensor specific, differences between how hardware records intensity of radiation… ask your local engineer
    Gain = is a multiplier
    Bias = is a shift (plus or minus)
    Mean solar exo-atmospheric irradiance – The irradiance from the sun at the top of the earth’s atmosphere… sun puts out a certain amount of power and…
    There are different ccalculations for that but we use one from Thuillier et al 2003
    All the metadata reports include solar elevation but what you need is solar zenith… which is 90-solar elevation (watch your units- radians vs degrees)

## Slide 5: Atmospheric Effects
  Another source of ‘noise’
  Atmosphere selectively scatters, absorbs and transmits light
Notes:     Scattered, absorbed or transmitted depending on EM wavelength, atmospheric path length and atmospheric conditions
    Atmospheric scatter adds brightness to a scene and to compensate, we will subtract brightness from the scene.
    For change detection, it may be most robust to correct imagery to surface reflectance by compensating for atmospheric effects.

## Slide 6: Surface Reflectance Correction Methods
A few approaches:
  Dark object subtraction (DOS)
  Atmospheric modeling
      Radiative transfer models
  Image-to-image normalization
      Histogram matching
      Regression using pseudo-invariant features
Notes: Two approaches for change detection:
Atmospheric correction: histogram minimum involves calculating stats for eacTry to remove the effects of the atmosphere or simply normalize one image to the other (slave image and reference image)
These are just a few examples…

## Slide 7: Dark object subtraction (DOS))
Dark objects can be deep lakes or very dark shadows
  DOS involves identifying the value associated with these areas and subtracting it from all pixels in the image.
Automated using RSAC tools…
Pixel Value
Frequency
Jump
DOS value
Notes:   Theoretically should have zero reflectance
Done for each band

## Slide 8: Masking
Clouds and their shadows
  Lead to false positives in change detection.
Snow and water
  Seasonal variation
  Result in false positives (If not part of your research question)

## Slide 9: Masking
Cloudy Landsat image
Clouds
Shadows

## Slide 10: Image preprocessing
Function Mask (fmask)
    Identify clouds, shadows and water- Memory intensive process
Exercises 1 + 2 – creating cloud-free composites in GEE

## Slide 11: Image preprocessing
Google Earth Engine can do all of the heavy lifting for us!
Eliminates the manual processing steps
Exercises 1 + 2 – creating cloud-free composites in GEE

## Slide 12: Demonstration
Cloud-free composites in GEE