## Slide 1: Introduction to Change Detection Tools
Instructor: Brenna Schwert
November 6-7, 2019

## Slide 2: Data Resources – For your own projects
There is preprocessed Landsat data all over the place!
  Analysis Ready Data (ARD)
  Level-2 Data Products
  Google Earth Engine
Ancillary Data:
    Landcover data (Landsat derived)
      NLCD
      Landfire
And many more…

## Slide 3: Data Resources - Disturbance Mapping Projects
USFS/partner programs
    Fire Mapping
      BAER (Burned Area Emergency Response), RAVG (Rapid Assessment of Vegetation after wildfire), MTBS (Monitoring Trends in Burn Severity) and more…
    Forest Health and Disturbance Monitoring
      FHTET (Forest Health Technology Enterprise Team)
More programs and partnerships
    USGS/NASA, research institutions, Google Earth Engine, etc.

## Slide 4: Fire Effects Data Products - BAER
Burned Area Reflectance Classification (BARC)
    1-7 days post containment
Notes: Delivered to BAER teams upon request. First approximation of burn severity which can be used to identify hazards from flooding, landslides, etc. BARC is classified dNBR difference image.

## Slide 5: Fire Effects Data Products - RAVG
RAVG Severity layers and tables
    30-45 days post containment
    All fires >1000 acres on USFS land
Notes: Primary audience for RAVG data are regional silviculturists who need to communicate yearly reforestation and restoration needs.
Uses established regression models that relate calibrated NBR difference layers to field plot data in order to estimate changes in forest inventory parameters such as canopy cover and basal area.
Data is available via the RAVG website which you can get to via RSAC websites.

## Slide 6: Fire Effects Data Products - MTBS
Burn Severity layers from MTBS
    Assessed 12-18 months post containment
    All fires >1000 acres on USFS land
Notes: Long term monitoring of fire severity effects. Thresholds applied to the calibrated NBR difference image to create fire severity maps with low, medium and high severity burns

## Slide 7: Near Real-Time Forest Disturbance Program MODIS-Scale Application
USFS RTFD program provides the state and local forestry aerial sketch-mapping community with timely information to assist in flight mission planning.
  Delivers near-weekly results (every 8 days) of change detection analysis
  MODIS-based, 500m resolution
  All land ownerships, but limited to forested area
  Will improve Aerial Detection Survey program efficiency
Missouri 2009 Storm Damage
Louisiana 2010 Forest Tent Caterpillar
Pennsylvania 2010 Forest Tent Caterpillar
Michigan 2009 and 2010 Forest Tent Caterpillar
MODIS Disturbance Detection:
Aug 29 – Sept 13, 2010 compositing period
Northern California fire scars
CO Mountain pine beetle

## Slide 8: North American Forest Dynamics (NAFD)
Forest Disturbance and Regrowth Data
  Products from analyses of Landsat time series
    Vegetation Change Tracker (VCT) Algorithm
    Data available for 55 areas in the US
  NAFD project summary and data access

## Slide 9: Hanson’s Map of Global Forest Change

## Slide 10: Tools for validation – TimeSync
Online tool facilitating human interpretation of Landsat time series
  Useful for:
    Validating change detection output
    Estimating change from samples
Users get to interpret both images and plots

## Slide 11: Land Change Monitoring System (LCMS)
The LCMS approach takes advantage of the differences between change detection methods by combining them using an ensemble classifier

## Slide 12: Image-Based Change Estimation (ICE)
What is it?
  Sampling approach using image-based interpretations to quickly estimate land cover and land use change
    When no change present, 5 points
    When change present, 45 points
      All points attributed with LULC
  Completed for all lower 48 states
  Interpretation cycle follows NAIP’s schedule
No change
Change

## Slide 13: Questions?
brenna.schwert@usda.gov