## Slide 1: Integrating Digital 3D Imagery in Geospatial Workflows
Mark Hammond mark.Hammond@usda.gov

## Slide 2: Housekeeping
  Question or comment?
    Questions in chat will be answered after presentation
  Closed Captioning available in the More Options menu

## Slide 3: Course Format & Learning Styles
Many different learning styles: visual, auditory, kinesthetic, etc.
Webinar format seeks to address a variety of learning styles
  PPTs, live demonstrations, step-by-step exercises
  Content may be repetitive for some people
  Feel free skip formats that don’t serve your learning style

## Slide 4: Webinar Overview
Mixed Format
  10:00am
    Presentation
    Demonstration
    Work on exercises 1-3: setting up Summit, importing block files, measuring heights
  1 pm
    Presentation
    Demonstration
    Work on exercise 4: digitizing with ArcMap and Summit combined
Instructor standing by to provide assistance as you work on exercises
This webinar is being recorded
Course Duration: 10 am MDT to ~ 4:00 pm Mountain Time.

## Slide 5: Course Format & Learning Styles
Many different learning styles: visual, auditory, kinesthetic, etc.
Webinar format seeks to address a variety of learning styles
  PPTs, live demonstrations, step-by-step exercises
  Content may be repetitive for some people
  Feel free skip formats that don’t serve your learning style

## Slide 6: What this course will cover
Introduce how we can see stereo from imagery
Notes: Will discuss some of the properties that will aid in understanding how we can view two ‘flat’ photographs in stereo
[click to bring up single point image]

## Slide 7: What this course will cover
Using stereo parallax to measure heights from photos.
lens
lens
Camera Station 1
Camera Station 2
Film Plane
Notes: We will cover a minimum amount of technical detail so that you can understand what Summit Evolution is doing, without needing the full technical knowledge.

## Slide 8: What this course will cover
How to digitize in stereo
Notes: How to take the information we are seeing in stereo into actionable data
[graphics appear automatically]

## Slide 9: What this course will cover
The FS digital 3D viewing software: Summit Evolution
Notes: Most importantly, we will make use of demonstrations and exercises to learn how to use Summit Evolution with ArcMap

## Slide 10: Selected Characteristics of Aerial Photos
… a VERY brief introduction …

## Slide 11: Aerial “photos”
Notes: I will use the terms aerial photos and aerial images interchangeably for this class. While there are some important differences, once they get to the point of using them in stereo, the properties that are important are the same whether they are collected using film or a digital frame camera.

## Slide 12: Requirements for Stereo
Date Agency Scale Roll-Frame
Date Agency Scale Roll-Frame
Date Agency Scale Roll-Frame
Date Agency Scale Roll-Frame
60% Overlap
Notes: There are a couple of basic requirements of imagery that allow us to see in stereo.
First, the imagery must have a minimum amount of overlap. The minimum is 50%, but typically it is collected with 60% or more. The reason we need this much overlap is so there is enough common area of successive images for viewing. Also, if only the edges of an image pair, say 10%, were overlapping, an object would be very difficult to see due to its displacement.
Newer sensors (pushbroom) attempt to replicate this with forward and backward viewing sensors, but some have difficulty seeing in stereo with data from these sensors.

## Slide 13: Requirements for Stereo
Notes: What is displacement, then?? Mention how the trees at the center are properly placed and looking upright, but as you move away from the center (also called the principle point), the trees ‘lean’ away, and they are also DISPLACED. Higher elevations are also displaced more as you move away from the center.

## Slide 14: Photo Geometry--Single Point Perspective
Distortion: noise due to lens imperfections, poor camera vacuum, paper shrinkage etc… Always a nuisance factor
Displacement: the result of projecting a 3-D world (with varying heights) on a 2-D surface from a single point perspective. Almost always a good thing
  Allows for stereo viewing
  Measurement of heights, volumes
  Very predictable: f(relief, camera height, proximity to PP)
Notes: Displacement: comes from taking items on the surface of the earth and placing them on a flat surface WITHOUT the typical process we use to make a map. The displacement in imagery is replicated on the computer screen, and mimics our natural depth perception to allow us to see in stereo.

## Slide 15: Relationship to viewing
Parallax: the apparent shift of something we are viewing when we move position. This gives us depth perception.
Date Agency Scale Roll-Frame
Date Agency Scale Roll-Frame
We can equate two adjacent photo center locations to our pair of eyes.
Notes: Parallax is the apparent shift of something we are viewing when we move position, and it is this property, along with displacement, that makes it appear as if we can see the objects in three dimensions.
To put it all together, when we take two consecutively capture images and view them simultaneously, we are looking at one capture with our left eye, and the other with our right, simulating how we can see depth perception in our everyday world.
We will put together parallax, displacement, and how we make use of these, here in a few minutes.

## Slide 16: For more information…
The tutorial has more information on photo characteristics, as well as a supporting exercise

## Slide 17: Summit Evolution
Introduction and Overview

## Slide 18: Stereo Viewing Overview Topics
Capabilities—what is stereo imagery good for?
Major Components (hardware/software)
System Requirements
Importing ‘block files’
Navigation/Interaction
Notes: These last two topics will be covered in the demo rather than in slides.

## Slide 19: Summit Evolution Capabilities
Digital 3D Imagery software provides the following primary functions:
  The ability to view and navigate in stereo
  Photo interpretation
  The capability to measure and collect geographic information in 3D including:
    Measuring heights, and
    Heads-up digitizing (with elevations!)
Notes: [go through the points]
For the last point: in order to record an elevation in the shapefile or feature class, you must set up them up to include Z values.

## Slide 20: Summit Evolution System Requirements
System (moving target):
  Computer req. (class 2 desktop minimum recommended)
  Video/graphics requirement
  ArcGIS: version agnostic
    Recommend 10.2 or later
Data:
  Oriented Stereo Imagery—specifically…
    Block files from Imagine’s Leica Photogrammetry Suite (LPS), or
    Project files from SocetSet, or similar photogrammetric software
    Can now also import from PhotoScan
  This is not a trivial requirement!
Notes: The reason system is a moving target is the continued improvement in 3D technology and software
Unlike our experience with Stereo Analyst, Evolution has a more stable set of requirements, and is not as dependent on your version of ArcMap.

## Slide 21: How stereo-ready imagery is created
Block File
Image list
Sensor info
Orientation info
Elevation file info
Datum and coordinate info
Notes: Do not need to know LPS to use Summit Evolution, but it helps if the block file experiences any errors, or if you need to create smaller (subset) blocks from the full dataset.
Once you have the data, you need something to view it with…

## Slide 22: Stereo Viewing—Red/Blue Anaglyph
Notes: Looking at hardware, let’s start with the simplest. Can be used with any computer monitor system; the glasses cost less than a dollar or using plastic glasses for a few bucks
Not always easy to see (depending on the imagery); darkens the colors;

## Slide 23: Stereo Viewing—Active Systems
Stylish 3-D Glasses
Stereo Images rapidly flicker to produce 3D image effect.
IR emitter
Notes: The active stereo system is the most commonly used due to its affordability. The monitor, emitter, and glasses can be had for around $500. For those who have not used one before, [describe how it works]
The only downside is that, due to the flicker in the glasses, it can cause eye fatigue for many users.

## Slide 24: Stereo Viewing—Passive Systems
3-D Glasses
Stereo Mirror Monitor
Computer needs higher-end graphics card.
Notes: A ‘passive’ system, such as shown here, works by using different polarizations for each eye; e.g. horizontal for the left eye, and vertical for the right. [explain how the mirror then works]
The main benefit is that there is less eye fatigue, so this system is good for production work. On the negative side: cost; more difficult to use as a day to day monitor, and now becoming harder to find, although the company that makes the stereo software is not importing them from a company in Germany.
However, while either of these systems are nice to have, can use the system sitting on your desktop right now. Anaglyph isn’t the best, but it works.

## Slide 25: Setup Options—Stereo Display
Red/Blue anaglyph glasses.
Cheap
Works with any graphics card
Relatively poor performance (dark, poor colors, etc.)
Shutter Glasses and Emitter.
Price ranges from $400 to $800
Newer models work with LCD monitors
Great quality
Big heavy glasses
Recommended for occasional but not full-time production use
Planar Stereo Mirror with Polarized Glasses.
Price ranges from $2,000 to $8,000
Excellent quality
Improved glasses
Recommended for full-time production use
Notes: Active stereo system: Should work with current class 3 desktops; class 2 may need a different graphics card; check the computer graphics card against the manufacture system requirements.
Planar stereo mirror: Have been out of production for a little while and might be found in secondary market. A German company recently began manufacturing these, and we are in contact with their reseller for the US to get price information.
BIG RECAP: the software and hardware work together to give us digital 3D viewing; need to do a little homework in selecting a monitor system, and ensuring that you have a graphics card that will work.

## Slide 26: Measuring Heights
How we can use parallax to our advantage

## Slide 27: A bit of theory
Parallax: the apparent shift in the appearance of an object due to the change in position of the observer
Notes: Describe parallax using the near and distant tree or items on the desk example

## Slide 28: Fundamentals of Digital 3D
Left Image
Right Image
T
B
In the stereo model, distance T is less than distance B and T appears (and is) higher than B. The quantity B – T is directly related to the height of the feature.
Notes: In stereo viewing, we have two successive images captured along a flight line. The tree of course has not moved, but due to the shift in position of the observer, the camera in this case, the tree now appears to lean in different directions. We will refer to them as the left and right images based on how they are displayed.
This is a type of displacement, and since we know the details of how these images were capture (such as the altitude of the plane, information about the camera, etc.) we can use this to estimate the height of an object.

## Slide 29: Fundamentals of Digital 3D
Left Image
Right Image
T
B
In the digital stereo view, the user must make X parallax (Z) adjustments to clearly see features at different elevations. The Z adjustments determine the elevation…
The X parallax is adjusted for the tree
Top.
Bottom.
Notes: In the stereo viewer, we move the objects along the X axis of the screen, so this is usually referred to as the X Parallax [FIND THE PROPER TERM!]
This is a basic generalization, but it holds true whether we are measuring heights, or looking to get ground elevations to either measure slopes or include them in our shapefiles.

## Slide 30: “Seeing” in stereo
(This is viewable with your anaglyph glasses)
Notes: Point out that we can use the scroll wheel to adjust the parallax and move the stereo cursor up and down to ‘place it on the ground’.
If we look a little closer to where the cursor is at… [advance to next slide]

## Slide 31: “Seeing” in stereo
(This is viewable with your anaglyph glasses)
Notes: If you are new to stereo, it does take a while to get used to seeing the height of the cursor.
If you have anaglyph glasses, you should notice a red cursor and a yellow cursor in the image. The challenge for new users is to be able to note when the cursor is ‘on the ground”, or when the two cursors are lined up.
One key is to relax your eyes, and let them focus on the ground. A similar situation that might help is when you are looking out of your car windshield when it could be cleaned. Your eyes can focus alternately on your windshield, or on the road in front of you like they should be!! This is similar; let your eyes focus on the terrain, and then as the two cursors approach each other, you will be able to see them more easily.

## Slide 32: “Seeing” in stereo
Left Image
Right Image
Notes: To check how close you are, you can use the view modes in the Image View toolbar. This allows you to view only the left or right image at a time, and is a good check to see how well you have done getting the cursor on your object.
For those transitioning from Stereo Analyst, there is no mode where all three windows are displayed simultaneously, but this is a useful compromise.
There are two different ways we can adjust the parallax; manually with the scroll wheel on the mouse, or we can let the software do it, either on its own or by using an elevation file

## Slide 33: X Parallax Adjustment Modes
There are three X Parallax Adjustment Modes:
Manual — you make the adjustments
Automatic — using an external DEM
Automatic — using image autocorrelation
 | Measuring Heights | Heads-Up Digitizing
Manual | Best | Too tedious
Auto w/DEM | No - won’t work | Best (if DEM is good)
Auto w/Img auto corr. | Possible, do not recommend | OK (esp. if no or bad DEM)
Notes: -- explain autocorrelation

## Slide 34: X Parallax Adjustment Modes
Manual Parallax Adjustment
  Best for measuring heights of features (e.g. trees)
X Parallax is adjusted to view the tree top and a point on the ground near the tree—provides a tree height of approximately 6.3 m (~20.6 ft)
Notes: This really only works if you have bare ground near the tree. If you want the height of a tree in an area with closed canopy, it can be a bit trickier
Using manual adjustment is not best when digitizing, particularly when you are capturing Z values.

## Slide 35: X Parallax Adjustment Modes
Automatic Parallax Adjustment using DEM
  Best for heads-up digitizing
The X Parallax is adjusted as you roam through the imagery based on the elevation provided by the DEM—quite fast.
The the X Parallax is adjusted to match the ground, and not features within the imagery.
Notes: Note the icon in the upper right; we will use this button to add a DEM in Evolution

## Slide 36: X Parallax Adjustment Modes
Automatic Parallax Adjustment using image autocorrelation
  Use for heads-up digitization if DEM is bad or missing.
The X Parallax is adjusted to match features as you roam through the imagery. This happens based on the software’s ability to locate the same feature on both images—can be slow and jumpy.
Also depends on having contrasting objects in the imagery to work well.
Notes: Image Correlation is an option when digitizing where a DEM is not an option. It is called ‘Snap Toggle’ in evolution, and should not be confused with snapping when digitizing in ArcMap. This mode compares the two scenes, and uses a correlation routine between the two to compare locations and try to match the locations in the pair.
Typically this works well, but if you have any area such as around this two-track where there is little contrast, it can have a difficult time with the correlation, as can sort of be seen here; you will be able to see it better in the demonstration.
Now that we have an idea of how stereo works, let’s look more at the interface

## Slide 37: Evolution Major Software Components (1)
Notes: When you first open Evolution, the tool bar can be rather intimidating at first glance. However, there are only a few of the toolbars that you will regularly use, and we can easily customize the toolbar to remove the one’s we do not need.

## Slide 38: Evolution Major Software Components (2)
Options
Scroll speed
Image adjustment
Elevation
Zoom levels
Notes: For now, we will look only at Summit Evolution; there are toolbars that are available in ArcMap as well, and we will look at these in the second session.
When I opened Evo initially, the first thought was that this had a lot of options, but it could be intimidating for a first time user. Found that we can easily remove and add toolbars to simplify the interface; also found that I really used a few tools regularly.
Options button (also in menu option);

## Slide 39: Customization
Notes: As I mentioned, you can customize which toolbars appear, and the first exercise will take you through reducing the number that appear.
Another advantage of Evolution is the number of input devices you can use, and the ease in customizing the buttons. Good if you have something other than a system mouse; but even the system mouse buttons can be reconfigured. Notice a coupel of things; you can use two mice at once with this; X-box controller too!!
[Point out that you can Export and Import settings in case you need to move to a different computer, or you have multiple users.]

## Slide 40: Navigation Tips
In the main Stereo Window:
To activate the 3D cursor, ensure the stereo window is active click the right mouse button.
To exit the stereo window, either
  Double click the right mouse button, or
  Press the “Esc” key
While in the stereo window, use the F5-F12 keys to set zoom level. Also:
  Page Up will zoom out
  Page Down will zoom in
Notes: So last, here are the basics for using the stereo window. By the time you complete the exercises, these will hopefully become second nature to you.
[go thru the first two main bullets, and the zoom function keys]
One set of keys we do not stress in the exercises, but are good to keep in mind, are the final pair. The page up/page down buttons allow finer control of the zoom level in Summit

## Slide 41: NAIP Statewide Stereo Imagery
Collected using the ADS100 pushbroom camera, but loads into Summit Evolution very efficiently.
State Vendor Stereo DSM
Connecticut Quantum Spatial FS FS
Delaware Quantum Spatial FS FS
Maine Surdex Corporation NRCS NRCS
Maryland Quantum Spatial FS FS
Massachusetts Quantum Spatial FS FS
New Hampshire Quantum Spatial FS FS
North Carolina Quantum Spatial NRCS
Rhode Island Quantum Spatial FS FS
Tennessee Surdex Corporatio FS
Vermont Quantum Spatial FS FS
Virginia Quantum Spatial FS
West Virginia Quantum Spatial FS FS
Notes: These are the states where we’ll be getting NAIP stereo.

## Slide 42: demo exercises 1 - 3

## Slide 43: Information Extraction from 3D Digital Imagery
Mark Hammond
Remote Sensing Specialist / Trainer
RedCastle Resources Inc., working onsite at
Geospatial Technology and Applications Center (GTAC)
(801) 975-3497
markhammond@fs.fed.us

## Slide 44: Our Data is Geospatial
The appropriate repository for storing and analyzing geospatial information is our GIS…
Forest Service GIS and Image Analysis
Notes: A basic function for those of us who work with remotely sensed data is extracting useful information that can be used in products.

## Slide 45: Photography Contains a Wealth of Information
However, the geometry of photos makes direct transfer of photo information to our GIS highly inaccurate…
Notes: This is strictly for uncorrected hardcopy aerial photography, since this is our source of stereo imagery. Each of the images shown here are prints from negatives, and are not geocorrected.
We can transfer some information directly from these; for example (next slide)

## Slide 46: Transfer Options
There are many options that have been developed.
Options vary in:
  Accuracy
  Ease
  Cost
Technology has, of course, greatly improved the access to information transfer.
Notes: In the analog days, we could use two consecutive images in a nice expensive machine like this, and transfer information directly to a map or other type of document.
If you have never had the chance to use one of these, don’t pass it up if you get a chance.
A little cheaper method; [next slide]

## Slide 47: Ocular Transfer to OrthoPhoto Quads
Delineations are completed on photos
Transferred by eye to the orthos
Hardcopy orthos can be scanned into GIS
  and then polygons digitized on-screen
Or lines can be digitized from hardcopy orthos using a digitizing tablet.
Notes: Is using a simple stereo scope like the one shown here. However, it may not be as accurate since the images are the map are not used directly together.
But in a pinch, these steps can be used to get data from image pairs into vector form.

## Slide 48: Digitizing
Use orthocorrected photos
Reduces time needed to go from image to vector
Heads-up digitizing remains
Can use a Wacom or similar monitor (if you have the budget) to reduce the time needed even more
Still working in a 2-D world
Notes: Another alternative, if we have a softcopy orthomosaic and GIS software, is heads up digitizing. This is still the easiest method, and works for most projects.
A touchscreen tablet makes the process go even quicker, but can be costly
Stereo can offer improved interpretation, and allow us to get elevation.

## Slide 49: Computer Stereo Systems
Greatly reduces the barriers between photos and GIS.
Allows stereo viewing and digital GIS data collection via a single interface.
Passive Glasses with a StereoMirror
Shutter Glasses with 120Hz Monitor
Notes: As we saw this morning, there are two main types of stereo hardware beyond using red/blue or red/cyan glasses;
[recap the advantages and disadvantages of each, and mention the passive systems are becoming available again.]
While the two points on this slide are the same for heads up digitizing, we also have the stereo advantage now

## Slide 50: Photo Interpretation
An often overlooked element of digitizing is interpretation. Stereo viewing can be a great aid in (understanding? Interpreting?) what is occurring on the ground.
Image interpretation skills you might use for a single photo are still important for digitizing in stereo:
Ground knowledge of the area
Interpretation skills
A sound scheme for your vector data
The GTAC Fundamentals of Image Interpretation tutorial can be a good refresher for those who need it.

## Slide 51: Digitizing in Summit Evolution
The main event!

## Slide 52: Why the new software
Request for Proposals held in 2015
Thorough review process completed
Main advantages of Evolution:
  Simpler install
  ArcMap version agnostic
  Loads imagery much quicker
  Major improvements with large blocks of imagery
Notes: For those who are used to using Stereo Analyst

## Slide 53: Heads-Up Digitizing in Summit Evolution
Uses the common ArcMap digitizing tools in conjunction with Evolution
The target file must be 3D (has to have the Z value included)
Can add a background image/map in ArcMap to assist in review
By default, the orientation of the ArcMap window will rotate to match Evolution
Notes: Last bullet: can be a bit of a nuisance, but not bad once you are used to it; can always go into the Layer properties and re-orient north to the top.

## Slide 54: Summit Options for Digitizing
Notes: “Why we found Summit Evolution attractive”
Discuss the myriad of options, and that these are covered in both the demo and exercises

## Slide 55: Summit Digitizing Toolbars in ArcMap
Notes: Discuss the myriad of options, and that these are covered in both the demo and exercises

## Slide 56: Digitizing Basics
In ArcMap, start an editing session.
Click on the Capture Coordinates button to get the two programs communicating
Make sure the Create option is chosen in the DAT/EM Capture Drawing toolbar
Open the Create Features pane, choose your feature, and then choose your Construction Tool
Notes: I am starting with the actual digitizing process; presuming at this point that we have already created a vector file in Arc that includes the ability to capture elevation information if we need it.

## Slide 57: Digitizing Basics
A single left mouse click starts the polygon and adds vertices…
…use Ctrl+Z to remove the last vertex…
… After you place the last vertex, press F2 to end the line or to close the polygon.
Move to Summit Evolution, and activate the Stereo View window by right clicking in it.
Add an elevation file if desired
Change the setting in the DAT/EM Capture Drawing toolbar to Modify to edit a vertex in the Stereo View
Notes: For the edit in the bottom half, emphasize that while we are using many settings in ArcMap, all of your editing should be done in the Stereo view in Evolution

## Slide 58: Digitizing in Summit Evolution
Demo - Exercise 4