## Slide 1: STEReO
Scalable Traffic Management for Emergency Response Operations

## Slide 2: STEReO Scalable Traffic Management
NASA’s UAS Traffic Management (UTM) System
Standardized platform for sharing operation information & data
  Operator intention, contingency plans, equipage
  Airspace constraints, manned operations, terrain, weather
  Enables coordination between operators & other stakeholders across multiple platforms
Goal: safe and efficient use of airspace
  Safe separation, performance requirements, highly-automated authorization
  Shared awareness

## Slide 3: STEReO Emergency Response Operations
In disaster events UAS could…
  Reduce danger, enhance effectiveness, and make relief operations more expeditious
  Provide highly deployable and cost-efficient remote sensing with capabilities not possible with manned aircraft
  Support a wide range of missions (e.g. search & rescue, logistics support, mapping, etc.)

## Slide 4: STEReO Emergency Response Operations
Existing challenges include…
  Limited communication and infrastructure
  A high degree of collaboration and manual coordination to deconflict airspace
  Remote sensing data can’t be received in a timely manner

## Slide 5: To what extent can a UTM ecosystem…
Reduce response times?
Enable large-scale aircraft operations?
Provide operational resiliency to dynamic changes during a disaster event?

## Slide 6: Reduce response times
A public safety USS can be used to communicate the essential information needed to make a timely response
Increase interoperability of UAS operations and data flows, regardless of platform
Collaborative tools to ingest remote sensing information and distribute a common mission operating picture for all stakeholders for strategic planning and decision-making
Notes: What, where, what direction, what altitude, and how fast?
  Pilots typically want to know the answer right away so that they may respond

## Slide 7: Enable large-scale aircraft operations
Allow for more efficient and effective coordination between manned and unmanned operations without compromising safety through shared awareness of airspace, mission objectives, assets
Leverage vehicle-autonomy technologies
  Detect and avoid, safe2ditch
  payload-directed guidance, onboard decision-making
UTM is a scalable, flexible, yet structured system
  Risk based approach where geographical needs and use cases will dictate the performance requirements for airspace operations
Increased interoperability allows for more cooperation/collaboration
Notes: The two ”UTM mantras”

## Slide 8: Provide operational resiliency to dynamic changes during a disaster event
Increased situation awareness and common operating picture allow for earlier detection and decision making
Standardized, cross-platform communication of changes
  Environment, operations, mission objectives
Scalable to size and complexity of operations
Utilize advanced communication/connectivity technologies for data exchanges and information sharing
Vehicle to vehicle communication, and onboard autonomy to ensure the safety and resilience of the operations under a UTM system

## Slide 9: Five Domains
UAS services
Data services
payload-directed flight
sense and avoid
crash management
Vehicle to vehicle
Network
Common operating picture
Tactical IAA
Fleet management
NASA research results
Subject-matter experts
UTM Services
Autonomy
Domain Expertise and Tools
Human Factors
Communications
STEReO

## Slide 10: Why NASA?
Extensive background in aeronautics, communications, and autonomy research
R&D partnership with the FAA
Impartial/objective research
Safety is paramount
Coordinate with government and industry
Pioneers in UTM research
STEReO as a ‘disruptive’ technology

## Slide 11: Why UTM?
First of its kind UAS traffic management system
Research effort that will inform policy
Collaborative effort between government, universities, and industry
Field tested system
Notes: - STEReO will be the first of its kind for public safety USS
Research effort that will inform policy and they have an opportunity to be a part of that
Collaborative effort with strengths from each entity
UTM is a field tested system with at least four years of flight tests exercised

## Slide 12: How you can help
Our goal is to use NASA technologies to improve emergency response operations
Provide subject-matter expertise
Participation in research goals
Joint work areas
  Use-case and conops development
  Simulation evaluation
  Flight test partner

## Slide 13: Target Milestones
California(?) Wildfire Flight Test
Florida(?) Hurricane Simulation

## Slide 14: Questions
joey.mercer@nasa.gov