## Slide 1: Fire Monitoring and Assessment Platform (FireMAP)
A More Responsive, Affordable and Safe Method for Mapping Wildland Fires.
Dale Hamilton
Northwest Nazarene University
Assistant Professor of Computer Science

## Slide 2: FireMAP
What do we mean by Wildland Fire Severity?
How are we working to map fire severity in a more timely, affordable and safe manner

## Slide 3: What is Wildland Fire Severity?
How much fuel (vegetation) did the fire consume?
    Burn Severity (Fire Effects – First Order)
      The effects that concern the direct or immediate consequences of fire, such as biomass consumption and crown scorch. (nwcg.gov)

## Slide 4: FireMAP Research Objective
Enable the acquisition, analysis and management of hyper-resolution imagery to map burn severity in a more responsive, affordable and safe manner than is possible with current methods.
Utilize Unmanned Aircraft Systems (UAS)
Hyper (excess) resolution
  Spatial
  Spectral
  Temporal
  Radiometric
Notes: Hyper (excess) resolution
  Spatial
    The pixel size is smaller than the object being observed
  Spectral
    Spectral bands are smaller than the RGB bands needed for humans to be able to observe an object
  Radiometric
    Humans can only observe 64 levels (6 bits) of intensity
  Temporal
    Can the date and time of imagery be determined by ecological need instead of when the sensor is available over the burn?
Radiometric
      8 bit images allow 256 levels of intensity
      Micro-MCA and BaySpec OCI-F can capture 8 or 10 bits. OCI-F – 60 bands
      JPG format compresses to retain 6 bits of information.

## Slide 5: How will FireMAP map wildland fire more responsively, affordably and safely?
Workflow developing in reverse – NASA funded
Ecoinformatics
  Acquisition, analysis and management of complex ecological data to provide actionable knowledge for ecosystem management
Action
Knowledge
Geoanalytics
Imagery
Sensor
Platform
Notes: Ecoinfomatics – acquisition, analysis and management of complex ecological data in order to provide actionable knowledge for ecosystem management.

## Slide 6: What actions do managers need to take?
  Write post-fire recovery plans
Update vegetation layers
Update fire history atlases
Suppress vs manage future fires
Notes:   Post fire recovery plans - Burned Area Emergency Response (BAER) Teams
  Actions that could/need to take place in order to:
    Improve ecosystem response and productivity
    Reduce future fire risk/hazard
    Reduce erosion – adverse sedimentation into neighboring hydrologic features
Update vegetation (fuels) layers to reflect impact of this fire.
  Fuels Specialists
  Model effect this burn will have on future fire behavior and effects
Update Fire History Atlases (Hamilton, 2014)
  Fire Ecologists
  Most land management units have spatial fire history going back decades (or more)
    Spatial and severity accuracy is suspect the older the data is
    Spatial extent of fires under reported on small fires (Morgan, 2014)
      Small fires are the most spatially and ecologically diverse acreage (Hamilton, 2014)
  Used to calculate Fire Frequency and Fire Regime Departure. (frcc.gov, 2014)
Suppress vs manage a fire: Let future fires burn or actively suppress?
  Incident Command Teams
  Ecosystems (flora and fauna) are fire adapted
  Do we need more fire (let it burn) or have we had too much (suppress it)

## Slide 7: What do we need to know?
Knowledge – awareness gained from information and experience
Where has a fire burned and how severe was it?
  Can fuel consumption be determined by amount and type of char and ash?
    Black ash – mostly consumed Hot
    White ash – more complete combustion Hotter
  Change in live vegetation?
    Change in Chlorophyll can be measured by reflectance
      Scorched vegetation?
    Reduction in upper layer canopy cover (frcc.gov)
      Classify on life form to differentiate tree canopy from grass/shrub
Notes: Knowledge – Classes needed to identify burn severity
  Black ash (Charred organic matter)
  White ash
  (complete combustion) most important. – can we infer soil heating?
  Scorched (unburned) vegetation
  dying - expected mortality increases severity
  Unburned live vegetation (herbaceous, brush, canopy)
  need current canopy cover to determine reduction or veg change
  need lifeform to get at canopy cover (conifer/deciduous = canopy, herb/shrub = no canopy)
  if conifer/deciduous island -> surface fire
  Unburned dead organic matter
  slash?
  Mineral soil / Rock

## Slide 8: Geoanalytics - Discovery of Patterns -> Knowledge
Look for patterns in the spectral response
Blue
Green
Red
NearIR
Ultra-violet
Notes: Bands are Landsat 7

## Slide 9: Geoanalytics - Discovery of Patterns -> Knowledge
Potential tools for measuring burn severity
Machine Learning – learn by example
Support Vector Machine (SVM)
K-Nearest Neighbor (KNN)
Notes: Information and experience
we’ve seen something like this before -> can

## Slide 10: Geoanalytics - Discovery of Patterns -> Knowledge
Look for spatial patterns
Notes: Reynolds Creek prescribed burn – 4000x3000 image taken at 400ft AGL

## Slide 11: Geoanalytics - Discovery of Patterns -> Knowledge
Can we leverage hyper-resolution imagery to quickly and inexpensively map burn severity?
How high of resolution is necessary (adds info)?
  Spatial
  Spectral
  Temporal
Notes: Hyper = excessive
Spatial
  Higher accuracy with hyper-spatial resolution. (Rango, 2009)
  Function of altitude and sensor
  Pixels small enough that they won’t contain more than a one kind of material.
    Just conifer or just black ash
Spectral
  Intensity (energy reflectance)
  Bands (center and range)
Temporal
  Optimal image acquisition delay span (how long after containment to take imagery)
  Time of day & weather (lighting and degrade info)
Radiometric (ignore)
  Are there more that 8 bits of useful information per spectral band, per pixel?
  If not, is it because the analog image isn’t mapped properly to the digital image? E.g., is the burn are indistinguishable from the shadow area because of lack of resolution, or poor camera settings prior to digitization?
  Micro-MCA and BaySpec OCI-F can capture 8 or 10 bits.
  Can see 6bits, but can move where that 6 bits is over wide range

## Slide 12: Geoanalytics - Discovery of Patterns -> Knowledge
Pre-processing to better enable classification
Software filters
  Resample imagery to optimal resolution
  Normalization
  Transformation
  Object detection
Structure
Post-processing to clarify classification.
  Noise Reduction (Salt and pepper effect)
  Object enhancement
  Output spatial resolution
  Islands
    Unburned vegetation type
Notes: Filters
  Resample spatially to optimal spatial resolution
    Other resolutions?
    resampled 120m burn image -> 240m = burn extent worked fine
    what about burn severity/white ash?
    Can dumb down resolution, but can’t increase. There is no cure for stupid
Mitigate the “Curse of Dimensionality” – if we only have 3 dimensions (rgb, not an issue) – higher w/ object classification
  Transformation
  Principal Component Analysis
normalization is a process that changes the range of pixel intensity values
Dimensionality reduction
  Transformation
    Hue Saturation Value – drop value, separable without it
  Principal Component Analysis
Structure
  Identify burn/unburn before white ash and veg type
  If this is a morning image and there’s a tree to the east, this might be a shadow.
Post processing
Object enhancement
  Morphology to Bring out white ash
Salt and pepper effect
  Morphology – dialate, erode, open, close, connected components
    Blurring (Median Blur Filter)
    Majority Filter (arc) or Area opening(matlab/OpenCV) - removes from a binary image all connected components (objects) that have fewer than P pixels
Output Spatial Resolution
  Depends on what we’re looking at
Islands – if it’s just tree, is it island or low intensity burn (with live canopy)
  Look for grass vs just conifer/disciduous

## Slide 13: Imagery – How much data is enough?
Spectral Resolution
  Multi-spectral vs Hyper-spectral
    Extent & Resolution
Spatial resolution
  Pixel size smaller than object we’re looking at
Temporal
  UAS - on demand but have to be there
  Manned or Satellite – expensive and non-responsive
Notes: Spectral Resolution
Multi-spectral - consumer grade cameras
  Color (Red, Green and Blue)
  Near Infrared
Hyper-spectral
  Extent
  wider range of the electromagnetic (EM) spectrum
  Including Shortwave Infrared?
    Get data we can’t get with multi-spectral
      NIR, swir, thermal
    Are there unevaluated bands that we can’t get with satillite?
  Resolution
    Narrower bands record smaller part of the EM spectrum
Spatial resolution
  Altitude (AGL) of 60 meters (200 ft)
    Spatial resolution < 5 cm/pixel
  Pixel size smaller than object we’re looking at
    At what resolution do we stop getting an increase in information
  Improve on what’s available
    satellite = 2.5m – 30m
    Aerial = .25 – 1m
  Georeference
    Where exactly is the burnt log I’m looking at in the image?
    Needed for multi-temporal sampling and mosaicing
    Need latitude, longitude, elevation and heading
    Pix4D
    Can use ArcGIS to georeference and mosaic
Imagery - temporal resolution
  UAS - on demand but have to be there
  Manned
    Availability
    Cost (10x UAS)
  Satellite
    Flyover frequency
    Cloud/smoke cover

## Slide 14: Geoanalytics – Spatial Resolution
Reynolds Creek Prescribed burn – 120m AGL – 6.4 cm/px
Notes: Reynolds Creek prescribed burn – 4000x3000 image taken at 400ft AGL
6.4 cm/px => tan(47) * 120m/2000px

## Slide 15: Geoanalytics - Spatial Resolution
Previous image resampled to 30 meter (Landsat) resolution
Notes: Reynolds Cr burn resampled to 30 meter Landsat (8x6) resolution.

## Slide 16: Sensor – Data Acquisition
Inexpensive color cameras
  Show Red, Green & Blue bands
  Mod to capture Near Infrared (NIR) band
Hyperspectral Camera - capture visible and NIR bands
  Capture more, narrower bands.
  Can it capture beyond Near Infrared
    Shortwave Infrared (SWIR) @ 2.09-2.35 μm
Notes: Sensor
  Inexpensive color cameras
    Show Red, Green & Blue bands
      Blue .45-.51 μm
      Green .52-.60 μm
      Red .63-.69 μm
    Capture Near Infrared (NIR) band
      Change filter to capture NIR instead/in addition to Red
      Near Infrared = .77-.90 μm
  Hyperspectral Camera - capture visible and NIR bands
    Capture more, narrower bands.
    Can it capture beyond Near Infrared
      Shortwave Infrared (SWIR) @ 2.09-2.35 μm
      Reflectance spectrum obscured by atmospheric obstruction
  Radiometric resolution
    10 bit sensors - Micro-MCA and BaySpec OCI-F
NIR – Pi NIR camera
RGB, NIR, SWIR used because that’s what atmosphere does not block for Landsat
are there other bands that would be helpful that are outside atmospheric window.
Micro-MCA and BaySpec OCI-F are 60 bands, 10 bit sensors.

## Slide 17: UAS – Just get the sensor up there!
Why Unmanned Aircraft Systems (UAS)?
Low altitude = High spatial resolution
Increased Availability - fly under clouds and smoke
Affordability
Fire fighter safety
Notes: Why Unmanned Aircraft Systems (UAS)?
High spatial resolution
  FAA ceiling 120 meters (400 ft) AGL
  Hyper-spatial resolution @ 30 meters (100 ft) AGL < 2.5 cm
  Increase the precision of estimates of key rangeland indicators (Rango, 2009)
Increase Availability - fly under clouds and smoke
  Temporal resolution determined by local unit
  Let ecological needs drive timing of image acquisition
    Get knowledge to managers when they need it
Affordability
  1/10 cost of Manned (USGS, 2015)
Fire fighter safety
  Won’t put personnel at risk
  First priority of every fire management activity (WFLC, 2014)
Contrast satellite and manned aircraft –
manned fly at 5000 ft
fixed wind airspeed preclude hyper-spatial
Manned Helicopter - $5k/day
UAS contract for much less
Phantom 3 - $1000
Performance
transmit imagery in flight. Process onboard or at ground station.
Safety – don’t put man in air or in burn.
Purchase limit on government cards is $2,500

## Slide 18: FireMAP Proof of Concept Results
Image taken by a DJI Phantom 3 at 120 meters (400 ft) AGL

## Slide 19: FireMAP Proof of Concept Results
Burn/unburned classification with SVM

## Slide 20: FireMAP Proof of Concept Results
Addition of high severity (consumption) from white ash classification with SVM

## Slide 21: Acknowlegements
FireMAP funding through NASA EPSCoR via the Idaho Space Grant Consortium
Northwest Nazarene University
  Barry Myers – Computer Science
University of Idaho
  Greg Donohoe – Computer Science
  Eva Strand – Forest, Rangeland & Fire Science

## Slide 22: Questions?