## Slide 1
SKY-C2 SR
Command & Control / Surveillance & Reconnaissance
Phase II Program Update
Christopher Rowley, Director of UAS & Geospatial Solutions at Skyward, Ltd.

## Slide 2
USDA/NIFA Phase II SBIR Project
Project Information and Initial Goals
National Institute of Food and Agriculture (NIFA) Funding Opportunity Number: USDA-NIFA-SBIR-005277
Phase I Period of Performance: 15 July 2017 - 14 March 2018
Phase II Period of Performance: 1 September 2019 – 31 August 2021
Topic: 8.1 Forests and Related Resources
Sub Topic: Developing Technology that Facilitates the Management of Wildfires on Forest Lands
  Research that provides systems for detecting and managing wildfires
  Systems for reducing fuel loads in forests
  Tools and equipment for improving the efficacy and safety of fire fighters on the ground and in the air
  Communication and navigation systems for improving the coordination of fire management activities
Four Years Ago…
System Purpose: Command and Control / Surveillance and Reconnaissance Focused
  Based upon United States Air Force (USAF) Distributed Common Ground System (DCGS) and Tasking, Collection, Processing, Exploitation, and Dissemination (TCPED) methodologies
  Surveillance and reconnaissance technology and techniques to provide decision makers with actionable information to enhance wildfire management
Systems/software architecture based on similar Department of Defense “PED” systems (e.g., Angelfire, USAF Blue Devil)
Architecture strives to be technology agnostic (i.e., plug-and-play platforms and sensors)
System also strives to be open source / Open architecture

## Slide 3
USDA/NIFA Phase II SBIR Project
Project Information and Initial Technical Goals (Cont.)
Methodology Behind our Technical Objectives:
  Use (mostly) existing Commercial Off the Shelf (COTs) solutions to…
  …layer standardized geospatial data, with…
  …common image and data formats…
  …on an integrated geospatial background
The operating concept strives to:
  Provide decision-makers with a robust, shared Common Operating Picture (COP)
  Facilitate decision making and action in real-time by providing actionable data and information
  Rely on an Intranet that doesn’t require outside communication links (i.e., cellular and internet), but can use when available
With the end goals of providing:
  The ability to track and visualize fire fighters and operational assets in real-time
  Visualization of ingress/egress routes, black zones, civilian structures
  A secondary means to visualize/confirm fire status and position (Serve as a Force Multiplier)

## Slide 4
USDA/NIFA Phase II SBIR Project
Primary Overall Program Goals & Key Takeaways
Systems designed to be a smaller footprint and less expensive option
  As compared to similar systems developed for Department of Defense Missions
  Entire system can be purchased by government or industry for >$100K or >~$200K (depending upon configuration)
  Skyward may also seek to operate the system in a service capacity
System is designed to be open & common standards, open architecture, and as plug-and-play as possible
  The prototype design resulting from this project is meant to be modified and built upon
Aircraft, sensors, communications and ground station are baseline systems
  Built with input from forest wildland fire management community
  More inputs are desired and needed to improve the system and its components
The system continues to grow and change through new programs
  TAK Integration in cooperation with the Colorado Center of Excellence for Advanced Technology Aerial Firefighting
  National Oceanographic and Atmospheric Administration (NOAA) upgrades: large scale imagery mapping, automated flood edge detection, automated identification of petroleum hydrocarbons on water and sediment, addition of field data collection devices
  Electrical Power Infrastructure Inspection: Adding inspection sensors to aid prevention of electrical pole/tower and brush fires by identifying partial electrical discharge due to deteriorating assets (i.e., insulators)
  Skyward is seeking partners and additional funding for enhancements and spiral development

## Slide 5
Overall System Design
SKY-C2 System Quick Look
Area of Operations
(Analyst Work Station)
(GCS Control Center)
Ground Control & Analysis Station (GCAS)
F-STAR
Platform Control
Sensor Control
Analysis
(SPADE/Pursuer)
Basic PED System Architecture
Prototype Concept Image
HybridProject
SuperVolo
HD40
F-STAR Patch Antennas
Aircraft: Hybrid (gas/electric) Fixed-wing VTOL
  7+ hour duration
F-STAR System: Firefighter tracking
  Radio signal
Trillium HD40 (EO/IR) 3-axis Gimbal Sensor
  Selected for demonstration
  Other sensors can be integrated
Ground Control & Analysis Station (GCAS)
  Platform Control
  Sensor Control
  SPADE Geospatial Database
  Pursuer Geospatial Visualization Common Operating Picture (COP)

## Slide 6
System Design (Phase II SBIR)
System Benefits & Capabilities
HybridProject / SuperVolo
Vertical Take-off & Landing (VTOL) for variable launch locations
Gas/Electric Hybrid
7+ Hours Flight Time
60+ mph
9,000’ + AGL capable
Fail safes against stalling
Batteries re-charge in flight
5 minute re-fuel/re-launch
8-pieces / 2 minute assembly
Highly durable composite/aluminum frame
Autonomous/Manual flight
Redundant/protected electrical systems
Tightly engineered
Single transit case for transport
Radio beacon transmits location and unit ID
Transmits to antenna onboard aircraft (~5 km range – currently untested)
Internal w/recharging capability + augmentation with external sources (i.e. CR123 pack)
Sub-bands within 900-950MHz Tx/Rx (RF)
Feeds into SPADE database/Pursuer for visualization on maps/imagery
New system currently in development in partnership with Spectra Research, Inc.
TAK integration underway
10x optical zoom visible camera
  720p Global Shutter Visible Camera
5x optical zoom uncooled LWIR camera
  FLIR Boson 640 with 15-75mm lens
Visible FOV: 54° – 4.9° / Digital to 2.5°
Thermal FOV: 29.0 - 5.9° / Digital to 3.1°
Best-in-class robustness and stability
Electronic stabilization and scene tracking
Day and night operations
850nm laser for precise and discreet pointing
Highly resistant to dust and water
Can be swapped for other options
Radio Frequency-based Firefighter Search, Track and Recovery (F-STAR)
Trillium HD40 (EO/IR) 3-axis gimbal sensor ball (LV-CZ-GS)
Ground Station Comms: MPU5 Radio, RF900, R/C, WiFi, USB, Ethernet
  Transitioning to Persistent Systems 120° Integrated Sector Antenna
  LTE Capable
Laptop w/ SwiftCore Flight Management Systems
  Highly flexible, real-time autonomous route planning
Laptop for sensor control and data visualization
Hardened transit case for quick set-up/tear-down
Internal cooling and power management
Highly mobile & field deployable
Ground Control Station
Control Center (GCS-CC)
Analyst Work Station
Laptop for SPADE database and Pursuer COP
Two-monitor set-up
Hardened transit case for quick set-up/tear-down
Internal cooling and power management
Highly mobile & field deployable
MPU5 High Power S-Band RF Module (RF-2150)
In aircraft and on ground
MIL-STD System
30+ miles transmission range
Data transmission / management for all systems
  Aircraft telemetry & control
  Sensor telemetry & control
  Streaming video
  F-STAR data
Transitioning to Persistent Systems 120° Integrated Sector Antenna

## Slide 7
SPADE Database & Pursuer COP
Background & Capabilities
Initially developed by the Air Force Research Laboratory (AFRL) Sensors Directorate (RY)
  Customized for forest wildland fire management and natural disaster missions
More than a decade of development and operational use
  Primarily Department of Defense applications (i.e., combat support and maritime drug interdiction)
View Live FMV & Other Data
  All SKY-C2 data is visible in near-real time (i.e., aircraft telemetry, video footprint, video data, F-STAR beacons)
  Over world map (i.e., NASA WorldWind) or map data loaded by users
  Show focused views Picture-in-Picture
  Layer EO/IR Full-Motion Video (FMV) feeds together
  Integration with TAK currently underway
View Multiple Imagery Feeds
  Different sensor types
  Different geographic areas
  Monitor simultaneously
  Multiple windows at once

## Slide 8
SPADE Database & Pursuer COP
Background & Capabilities (Cont.)
Load .KMZ and 3D Structure Models
Load Shapefile layers
Load 3D Terrain, image & Map Data
Adjust Image Properties on the Fly
Set Watch Boxes and Trip Wires
Create, Monitor, and Save Tracks of Movement
Manual/Automated visual tracking, Multi-sensor display, geospatial data, playback historic data, etc.

## Slide 9
R/F-based Firefighter Search, Track & Recovery (F-STAR)
Prototype System Capabilities
Each firefighter can be equipped with an RF-based beacon providing a unique asset identifier (AID) coupled with GPS-based time and latitude/longitude coordinates
Body-worn beacon will communicate with an airborne platform via a transmitted UHF signal (900-950 MHz)
Beacon is a self-contained device consisting of:
  Custom designed embedded antenna(s); Internal GPS receiver; Microcontroller electronics; Mode select buttons; Charging/programming port; Mounting strap loophole; Rechargeable Li-Ion battery; Integrated “emergency beacon” mode to alert ground station with increased RF-ping/reporting rate; System will be rated at IP67 to prevent dust and water ingress
Emergency beacon mode increases radio ping frequency (i.e., more/faster pings); creates alert w/in Pursuer COP
Conceptual form-factor does not represent the final design topology
  Pending inputs from operational community
Upgrade: Additional optical mode (optical/IR strobe) is planned to augment detect, locate, and identification functionality
  Possible IR mode will incorporate a light emitting source (LED cluster) that can be captured by any IR sensor
  A unique flash sequence can be used to discriminate the LED cluster from ambient light sources such as fire glint or sunlight reflections
Parameter | F-STAR Goal
Mode(s) | Radio Frequency (RF)
Detection range | 5 km (RF)
Power | Internal w/recharging capability + augmentation with external sources (i.e. CR123 pack)
Size | <16 in3 (firefighter) <50 in3 (airborne)
Operating frequency | Sub-bands within 900-950MHz Tx/Rx (RF); Visible (optical)
Data transfer | GPS coordinates with ID string up/down echelon
Data protocol | Compatible w/required apps (Pursuer, SPADE)
Environmental | IP67 or better

## Slide 10
R/F-based Firefighter Search, Track & Recovery (F-STAR)
Prototype System Capabilities (Cont.)
A separate RF transceiver system (+ antenna) is onboard the airborne platform
The RF transceiver module will receive data strings from each beacon
  Data parsed via onboard microcontroller and transferred via common communication bus to the onboard radio system (i.e. MPU-5) for downlink transmission to the ground station
RF transceiver operates in the same UHF band as the firefighter beacon, whereas the downlink transmission will occur via a secondary band (2.4 GHz) using MPU-5 radio
RF transceiver module is mounted at the bottom of the platform fuselage
  Nested inside carbon fiber frame inside of protective cowling sleeve
Upgrade: Note that other critical parameters and biometrics can be integrated into future beacon designs
  Local temperature, CO2 content, atmospheric pressure, as well as firefighter vitals consisting of heart rate, body temperature, etc.
Patch Antenna (RF Transceiver) Example
Aircraft Fuselage

## Slide 11
Pursuer COP
F-STAR Data Visualization
F-STAR Beacon locations will be displayed within the Pursuer COP
Data Layer can be turned off and on
F-STAR Emergency Beacon Mode
DCYPHERS
Hover cursor for info
IR Strobe will be visible in IR video
Pings (w/ tracks) appear on map at GPS location of beacon
Pings update according to user-defined settings (e.g., every 4 seconds)
F-STAR emergency beacon mode sends rapid more pings, changes dot color, creates flag
Hover cursor over dot for information (i.e., unit ID, coordinates, elevation)
F-STAR data will be separated into layers by unit and individual beacon
Future enhancement: Optical/IR strobe for visual identification

## Slide 12
Hybrid Project SuperVolo
SuperVolo (2.0)
SuperVolo Specifications and Capabilities
Vertical Take-off & Landing (VTOL)
Gas & Electric powered (Hybrid)
  Gas motor charges batteries during flight
SuperVolo (1.0) |  | SuperVolo (2.0)
Category | Current | Upgrade (Estimates)
Endurance | 6.5 Hours | 7.5 Hours
Speed | 45-65 mph (72-105 kph) | 45-65 mph (72-105 kph)
Wingspan | 107 in (2717 mm) | 120 in (3048 mm)
Length | 72.5 in (1842 mm) | 72.5 in (1842 mm)
Weight (Empty) | 25 lbs | 26 lbs
Weight (Maximum) | 35 lbs | 38 lbs
Useful Load | 10 lbs (6.7 fuel + 3.3 payload) | 13 lbs (8 fuel + 5 payload)
Fuel Capacity | 1 US Gal (3.8 L) | 1.25 US Gal (4.7 L)
Fuel Type | Pre-mix gasoline / 40:1 (gas/oil) | Pre-mix gasoline / 40:1 (gas/oil)
Sensor(s) | Sony Mapping Camera | Lucint12* & Trillium HD40
Lucint 12 (*future Plan)
Trillium HD40

## Slide 13
Hybrid Project SuperVolo
Benefits and Fail-safes
Robust VTOL-quad functions independent of fixed wing as failsafe measure
  Turn on quad rotors at any time to take over flight
  Quad tested and proven effective in 40 mph winds
Sophisticated engine management system optimized to address in-flight problems
  Constantly seeks to restart unless otherwise directed
Can transition to glide to reach closest established rally point in the event of complete failure
Automated failsafe will correct aircraft and automatically land during failed take-off attempts
Hand controller unit can override all systems if needed
  Tested out to 15 km
  Improves battery economy in cases where batteries are low
Autopilot system has redundant auto-switching between power supplies
  Runs primarily off of battery power; switches to electric supplied by gas motor as needed
Surge protection built between all major components
  13 power isolated circuits w/ 2 amp breaker to isolate shorts and protect overall systems
  Tested in rain for 1 hour+
Custom designed autopilot carrier board integrated with U.S. made Pixhawk Cube

## Slide 14
Communications
Persistent Systems Radios, Planned Upgrades & Internet
Aircraft houses the Persistent Systems Wave Relay Embedded Module
  Transmission of all aircraft, sensor and F-STAR data
  2.4 GHz radio transmission
Ground Station houses an additional RF Module and MPU5 Radio chassis
  Upgrade to Persistent systems 120° Integrated Sector Antenna which will significantly increase range and sector swath
Sierra wireless AirLink LX60 Dual Gb Ethernet LTE Router
  Provides internet to workstations when LTE signal is available
  Internet connection provides ability for remote pilot to access aircraft via secure VPN; aircraft can be flown from anywhere in the world; manufacturer can access aircraft for in-flight troubleshooting
Sierra wireless AirLink LX60 Dual Gb Ethernet LTE Router
Persistent systems 120° Integrated Sector Antenna
Persistent Systems MPU5 High Power S-Band RF Module (RF-2150)
Persistent Systems Wave Relay Embedded Module System

## Slide 15
Automatic Dependent Surveillance–Broadcast (ADS-B)
FAA Rules & Current Approach
Discussions with FAA indicate ADS-B systems are currently not allowed for use on sUAS
From the regional FAA office in Cincinnati, Ohio
  “Current thinking is that ADS-B Out should not be used on Part 107 aircraft unless specially authorized. There is a frequency congestion issue that requires us to confine ADS-B-out to manned aircraft. Upcoming rulemaking will likely make the prohibition on ADS-B-out explicit. In situations where ADS-B Out is required, it must meet one of two standards to comply with the 2020 mandate:”
    “Mode S transponder with Extended Squitter, referred to as 1090ES; meets performance requirements of Technical Standard Order TSO-C166b”
    “Universal Access Transceiver (UAT); meets the performance requirements of TSO-C154c*. and operates on 978 MHz.”
For this reason, Skyward did not include an ADS-B transmitter onboard the aircraft
If desired, Skyward can integrate the PingRX (by uAvionix) ADS-B (in) receiver onboard the aircraft to collect and visualize signals broadcast from other aircraft
Currently working to push aircraft position data into TAK as a reporting mechanism

## Slide 16
Ground Control & Analysis Station (GCAS)
Components
Ground Station contained in 4 total transit cases (+1 for aircraft)
Rapid set-up and tear-down (<1 hour)
Not all equipment is required for the ground-station
  Developed and optimized to support a full-up crew (Pilot, sensor control, analyst, IT support, aircraft maintainer)
Desk Configuration
Pelican fold-out desks
Bluetooth Keyboard and mouse
Headsets with mic
USB Extender cord for headset
Dual monitors w/ desk-clamp stand
Desk lamp
Mouse pad
Rack Case Configuration
5U Transit Case
3 Laptops (1U)
1 UPS (2U)
3 docking stations
6 HDMI cables (monitors)
3 USB extender cables (headsets)
Cable Management
Aircraft Control
Sensor Control
SPADE/Pursuer Analysis
At All Workstations

## Slide 17
Overall Data Flow
Systems and Communications
Note: On-aircraft LTE will not be available on the Phase II demonstration build, but is an option for future systems
Aircraft take-off and landing can occur via “Orange Box” comms or from Aircraft Control Workstation
  “Orange Box” can be deployed to field for remote take-off and landing; hand-off to Aircraft Control Workstation after take-off
Ground-based MPU5 to be replaced by Persistent Systems 120° Integrated Sector Antenna
All software functions can be performed on a single laptop if desired

## Slide 18
Concept of Operations (CONOPs)
Employment Methodology
Area of Operations
Can forward deploy aircraft and pilot for quick take-off/landing and recovery or fly to FTA from ~20 miles away
VTOL allows for variable take-off/landing locations
Refueling and re-launch is possible in under 5 minutes
Aircraft can autonomously loiter on a circular surveillance track, fly waypoints, execute a mapping grid and download data in real time
Can operate from 0-5,000’ (+) AGL within or above Fire Traffic Area
Provides EO/IR Full-Motion Video (currently)
EO/IR Video
F-STAR system provide location data and unit ID to aircraft-mounted antenna
Up to ~5km from aircraft (currently untested)
GCAS
Data transmission between aircraft and GCAS via MPU5 High Power S-Band RF Module (RF-2150) & 120° integrated sector antenna
~30 mile range
Aircraft and sensor telemetry and control
Video and F-STAR data transmission
LTE option for aircraft telemetry and control is not planned for inclusion under this project, but is available
GCAS can be field deployed or can reside ~30 miles away
Provides independent control for aircraft and sensor
Dedicated analysis work station for product development & real-time visualization in context with other geospatial data
Mobile, hardened

## Slide 19
Future Developments
Future Enhancements Available Through Parallel Efforts
Skyward was awarded a Phase I SBIR by the National Oceanic and Atmospheric Administration (NOAA)
  Processing, Exploitation and Dissemination (PED) System for Rapid Response to Disasters
  Proposal scored a 95% by reviewers
  Phase II application submitted in February 2021
Skyward proposes use of the same PED system for NOAA-related natural disaster response
  Phase I research focused on design enhancements to the current system
  Some enhancements may be useful to the forest wildland fire management community
  Planned Enhancements: large area rapid mapping camera, automated flood edge detection, automated detection of petroleum on water and sediment, field data collection tablets and software, data sharing
Seeking additional funding (possible USDA Phase I SBIR) to develop new real-time automated fire line detection and reporting system
Lucint32 Vision Mapping Camera
Paired with Hybrid Project SuperVolo UAS
High-resolution large area mapping
Download and stitch maps in real-time
EO/IR/MSI capable
~10,000 acres per hour (15.6 sq miles)
3-5 cm spatial resolution
Multiple lenses for various alt. available
Co-mounted with Gimbaled Video
Main Pursuer COP
Deployed Tablets
SPADE
Other Orgs Databases
Other Orgs Databases
Other Orgs Databases
Database Sharing & Visualization

## Slide 20
What Will Be Demonstrated
Goals for Phase II Demonstrations to Fire Management Community
Full System Demonstrations Planned for July & August 2021
Demonstrations are currently planned to occur at Springfield Beckley Municipal Airport, Ohio
  New Beyond Visual Line of Sight (BVLOS) test range
  In partnership with the Air Force Research Laboratory, Ohio Department of Transportation (ODOT) and Ohio UAS Center
  VLOS Area: 7 nm² box (0’-3,500’ AGL); BVLOS Area: 200+ nm² area, (~1,000’-’10,000 MSL) / 500’ buffer below, 2,000’ buffer above
  17 mile long corridor
Demonstration Goals Include:
  Aircraft flight characteristics and capabilities (i.e., VTOL, hybrid, multi-communications, control swapping, distance, duration, etc.)
  Aircraft control from remote location
  Rapid recovery, re-fuel and re-launch
  BVLOS communications and data transmission
  Data receipt and visualization
  F-STAR visualization, tracking, and emergency beacon
Springfield Beckley Municipal Airport VLOS/BVLOS Range

## Slide 21
Contacts
Skyward Team
Christopher Rowley, Director of UAS Operations
  crowley@skywardltd.com
  937-252-2710 Ext. 110
John Haas, Vice President Technical Services
  jhaas@skywardltd.com
  937-252-2710 Ext. 104