## Slide 1: Supporting RxCADRE Fire Measurements Unmanned Aerial Systems
TFRSAC, Moffett Field, CA
April 17, 2013
Thomas Zajkowski; RedCastle Resources, USFS Remote Sensing Applications Center, Salt Lake City UT
Otto Martinez, William Holley, Alexander Paxton; USAF AFMC 96th TSSQ/RNXT, Niceville FL
John Hiers; Air Force Wildland Fire Center, Jackson Guard, USAF AFMC 96th CEG/CEVSNP, Niceville FL
Matt Dickinson; USFS Northern Research Station, Newtown Square PA

## Slide 2: RxCadre 2011
RxCADRE – Prescribed Fire Combustion Atmospheric Dynamics Research Experiments
Eglin AFB February 3-6, 2011.
3 UAS – USGS Raven, Prioria Maveric, G2R
Flights were successful, demonstrated that sUAS is capable of collecting scientific measurements over controlled burns

## Slide 3
Fuel Characteristics
Local Event-Scale Meteorology
Fire Behavior
Fuel Consumption
Event-Scale Fire Mapping
Emissions & Event-Scale Plume Behavior
Fire Effects
Mass
Cover
Depth
Moisture
Plume properties
Fine-scale wind & thermodynamic fields
Fire intensity
Rate of spread
Convective/radiative power & energy
Soil heating
Wind/flame velocity
IR imagery
Mass consumed by fuel component
Fire radiative power & energy
Flame front development
Satellite imagery of fire behavior and effects
1
2
3
1
3
6
4
Thermal radiometry
HD visual imagery
Stem temperatures
5
CO, CO2, H2O, PM2.5
Black carbon
Plume height
Pre- and post-fire LiDAR collection (manned)
Active-fire smoke sampling (UAS and manned)
Rx-CADRE Airborne Measurements - overview
Airborne: UAS and/or manned platform
Active-fire IR/visible mapping (UAS and manned)
Satellite: MODIS, VIIRS, MISR
Satellite (MODIS, VIIRS)
Satellite (MISR)

## Slide 4: 3 Types of UAS
Scout
G2R
Scan Eagle
Additional aviation assets
Cessna 337 – Smoke Sampling
Piper Navajo – Fire Imaging
EPA Tethersonde – Smoke Sampling

## Slide 5
30 m met tower
Rx-CADRE Active Fire Measurements – Large Units (500-1000 acres)
Active fire measurements
Ground-instrument cluster
~ 50 – 100 ft AGL
~650 ft AGL
~1100 - 3000 ft AGL
~4,100 – 10,000 ft AGL
NOTE: Cessna 337 smoke sampling aircraft is downwind following plume ~1000 - 8000 ft AGL
UAF Scout – LWIR, Flight 1 HIP-3, Flight 2 as directed
EAFB Test Wing G2R1, G2R2 – LWIR smoke sensor, wind, T, and RH sampler, F1 HIP-1, HIP-2; F2 MAPPS
U. Alaska ScanEagle – LWIR synoptic view
Piper Navajo – WASP sensor (LWIR/MWIR/SWIR and visible fire mapping at zenith)
UAS
Manned
>2000 ft separation
10 m met tower
~600 ft AGL
500 ft. lat separation

## Slide 6: B70L2G Manned/Unmanned Schedule November 10, 2012 V2
1000 Launch Weather Balloon 1
1000 Get MAPPs and Thethersonde coordinates.
1100 Launch Scan Eagle (SE)—1500 AGL
1115 Launch Low Manned (LM) (Urbanski, Smoke Sampling)
1130 Launch High Manned (HM) (Kremens, WASP)
1150 Low Manned begins sampling over B70L2G once SE Upwind LG1
1220 IGINITION
  Launch Scout
  Raise Tethersonde to 300 ft. AGL
  Launch G2R1
  Launch G2R2
  LM Cleared to Orbit as desired North of Range Downwind
  HM Orbit 6000 – 10000 ft. AGL over L2G
  SE Orbit 1100 – 3000 ft. AGL over L2G
  G2R1 – G2R2 Orbit 600/650 ft. AGL , 500 ft. lateral separation over HIP 2 – 3
  Scout Orbit 50 – 100 ft. AGL HIP – 1
1235 Retrieve Scout once HIP – 1 is burned over
1235 Focus SE imagery over MAPPS
1240 Re-launch Scout (As needed / Directed)
1242 Satellite Overpass VIIRS
1243 Satellite Overpass MODIS
1245 Retrieve G2R1
1300 Retrieve G2R2
1305 Burnout Complete
  Retrieve SE once LM confirms it is clear of B70 (Tree Line) or above 5000 ft. AGL
  Retrieve G2R1
  Release HM
1330 Lower Tethersonde
  Confirm LM has departed
  Confirm HM has departed B70
  Confirm SE has landed
  Confirm no RxCadre Aircraft Manned/Unmanned are airborne
  1400 Launch Weather Balloon
  1430 Release Airspace
All times approximate, based upon ignition time

## Slide 7
Test Area B-70
B-75
B-82
UAS Launch \ Recovery
Tethersonde Balloon
30 meter tower(MAPPS)
N
1
3
HIP
2
L1G
L2G
Scout Launch \ Recovery
B70L2G Air Plan 10Nov12
LM Profile (Approximate)

## Slide 8
N
0.6 miles
S
A
B
C
D
B-70
2
B-82
Natural Pine HIP
Aerostat Balloon
30 meter tower Burn 1
1
3
2
3
Oak HIP
Managed Pine HIP
1
30 meter tower Burn 2
Burn Block L2G
Burn Block L2F
30 plot grid lines

## Slide 9: Scout Imagery

## Slide 10: Scout TIR Imagery

## Slide 12: Scan Eagle Video

## Slide 13: Scan Eagle TIR

## Slide 15: G2R Video

## Slide 16
Hot Targets
Sarnoff TerraSite Output S-5

## Slide 17
S5_18:15:58 – 5210 M², 1.28737 Acres

## Slide 18
S5_18:15:58 – 5210 M², 1.28737 Acres

## Slide 21: G2R Meteorological /Black Carbon
Delivered as kmz, shapefiles, txt???

## Slide 24
B70CL1G
G2R
Smoke Sampling
Scan Eagle
Mosaics
Stills
G2R
Scout
Scan Eagle
EO Video (RAW)
G2R
Scout
Scan Eagle
IR Video (RAW)
G2R
Scout
Scan Eagle
RxCADRE 2012
TerraSite Processing
3D Mosaic Processing
G2R
Specs
Scan Eagle
Specs
Scout
Specs
UAS DATA PLAN V2
Air Plan

## Slide 25: Comments/Questions
Thank you to JFSP for funding this project.